## Slide 1
Yellowtail Dam & Bighorn Lake Operating Criteria Review
Billings, MT
September, 2010
RECLAMATION
Managing Water in the West

## Slide 2: Bighorn Lake Operations
Revised Operating
Criteria Review

## Slide 3: RESERVOIR TARGETS
Date Existing Proposed Difference
_______ Targets Targets (feet)
Oct 31 3635 3638-40 +3-5 ft
Nov 30 3630 Eliminated
Mar 31 3605-14 3617-21 +7-13 ft
July 31 3640 3640 Same

## Slide 4: Nov-Mar Release Calculation
Water Balance Equation Used to Calculate Nov-Mar Release Rate Based On:
  Nov-Mar Release from Buffalo Bill and Boysen Reservoirs
  Forecasted Nov-Mar River Gains
  Draft Reservoir to near Elevation 3617-3621 by March 31
  Preference to River Flow before reducing releases below 2000 cfs
  Preference to Lake Level before increasing releases above 2500 cfs
  Minimize reductions in River Release.

## Slide 5: 2009 Rule Curve using Actual Inflow

## Slide 6: Spring Runoff Forecasts
April-July Inflow % of
Date Forecast (ac-ft) Average
Feb. 1 634,000 57%
Mar. 1 591,000 53%
Apr. 1 625,000 56%
Apr. 15 730,000 65%
May 1 900,400 81%
May 15 1,121,400 101%
June 1 1,263,300 113%
Actual 1,504,354 135%

## Slide 7
Chart: Bighorn Lake Forecasted April-July Inflow
| 1-Feb | 15-Feb | 1-Mar | 15-Mar | 1-Apr | 15-Apr | 1-May | 15-May | 1-Jun | Actual
 | 634000 | 634000 | 591000 | 591000 | 625000 | 730000 | 900400 | 1121400 | 1263300 | 1504354
Average | 1120000 | 1120000 | 1120000 | 1120000 | 1120000 | 1120000 | 1120000 | 1120000 | 1120000 | 1120000

## Slide 8
Chart: Bighorn Lake Rule Curve Operation 2010

## Slide 9
Chart: Bighorn Lake Rule Curve Operation Continuing 2,750 cfs Release through April, 2,500 cfs through May 15 and 9,500 cfs from May 15-June 30
Forecast Elev | 3641 | 3641 | 3641 | 3641 | 3640.9 | 3640.9 | 3640.8 | 3640.7 | 3640.6 | 3640.4 | 3640.3 | 3640.1 | 3640 | 3639.8 | 3639.7 | 3639.5 | 3639.4 | 3639.3 | 3639.1
Forecast River | 4500 | 4500 | 4500 | 4500 | 3500 | 3500 | 3500 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000

## Slide 10
Chart: Bighorn Lake Rule Curve Operation Continuing 2,750 cfs Release through April, 2,500 cfs through May 15 and 9,000 cfs from May 15-June 30
Forecast Elev | 3643.6 | 3643.6 | 3643.6 | 3643.6 | 3643.5 | 3643.5 | 3643.4 | 3643.3 | 3643.2 | 3643.1 | 3642.9 | 3642.8 | 3642.6 | 3642.5 | 3642.4 | 3642.2 | 3642.1 | 3642 | 3641.8
Forecast River | 4500 | 4500 | 4500 | 4500 | 3500 | 3500 | 3500 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000 | 3000

## Slide 17: End of September Storage
Storage Lake Elev.
Water Yr Acre-feet Feet
2011 965,000 (est) 3630.5 (est)
2010 1,060,795 3639.3
2009 1,067,768 3639.8
2008 956,743 3629.7

## Slide 18: Nov-Mar River Release Spreadsheet

## Slide 20: QUESTIONS & COMMENTS