1)	What is the frequency of occurrence for flood control releases within and between years below project dams (Shasta, Whiskeytown, Nimbus, Oroville, and New Melones) over the duration of the proposed long term OCAP ?

The time period chosen was from water year 1978 to 2002 for the analysis of flood flows with the exception of New Melones which did not come online until the summer of 1979.  Daily average release to the river from Keswick, Whiskeytown, Natomas, and Goodwin were used for the Reclamation reservoirs.

# Keswick Releases

The following analysis classifies a flood release for Keswick as having the following criteria: (1) Shasta Reservoir is encroached according to the Flood Control Diagram dated July 8, 1977, and (2) the release to the river from Keswick be greater than 16,000 cfs because the operator is bypassing the capacity of the Keswick power plant.  Figure 1 shows the timeline of Daily Average Keswick Releases from Oct 1, 1977 to Sep 30, 2002.

Table 1. Days in Flood Control for Shasta and 40-30-30 Index from Water Year 1978 to 2002

| Water Year | Days in Flood Control | 40-30-30 Index |
| --- | --- | --- |
| 1978 | 19 | AN |
| 1979 | 0 | BN |
| 1980 | 39 | AN |
| 1981 | 0 | D |
| 1982 | 73 | W |
| 1983 | 88 | W |
| 1984 | 59 | W |
| 1985 | 0 | D |
| 1986 | 36 | W |
| 1987 | 0 | D |
| 1988 | 0 | C |
| 1989 | 0 | D |
| 1990 | 0 | C |
| 1991 | 0 | C |
| 1992 | 0 | C |
| 1993 | 17 | AN |
| 1994 | 0 | C |
| 1995 | 72 | W |
| 1996 | 35 | W |
| 1997 | 61 | W |
| 1998 | 59 | W |
| 1999 | 42 | W |
| 2000 | 39 | AN |
| 2001 | 0 | D |
| 2002 | 0 | D |

Figure 1.  Keswick Releases from 10/1/1977 to 9/30/2002

# Whiskeytown Releases

Flood releases from Whiskeytown were those that were greater than the minimum instream flows that were proposed in May 1963 up to water year 1995 where the flow requirements switched to the 3406(b)(2) Biological Opinion flows, and water was being released through the spillway.  Table 2. shows the total number of days that flood flows occurred and Figure 2 shows the daily average releases from Whiskeytown.

Table 2. Days in Flood Control for Whiskeytown and 40-30-30 Index from Water Year 1978 to 2002

| Water Year | Days in Flood Control | 40-30-30 Index |
| --- | --- | --- |
| 1978 | 5 | AN |
| 1979 | 0 | BN |
| 1980 | 0 | AN |
| 1981 | 0 | D |
| 1982 | 63 | W |
| 1983 | 81 | W |
| 1984 | 0 | W |
| 1985 | 0 | D |
| 1986 | 17 | W |
| 1987 | 0 | D |
| 1988 | 0 | C |
| 1989 | 0 | D |
| 1990 | 8 | C |
| 1991 | 0 | C |
| 1992 | 0 | C |
| 1993 | 10 | AN |
| 1994 | 0 | C |
| 1995 | 14 | W |
| 1996 | 0 | W |
| 1997 | 5 | W |
| 1998 | 8 | W |
| 1999 | 0 | W |
| 2000 | 0 | AN |
| 2001 | 0 | D |
| 2002 | 0 | D |

Figure 2.  Whiskeytown Releases from 10/1/1977 to 9/30/2002

# Oroville-Thermalito Releases

The time period chosen was from water year 1981 to 2002 for the analysis of flood flows.

The following analysis defined a flood release event as a day when the Total Feather River release was greater that 10,000 cfs and releases through the low flow channel was greater than 650 cfs.  Figure A.  shows the timeline of Daily Average Feather River Flows from Oct 1, 1980 to Sept 30, 2002.

Table 1.  Days in Flood Control for Oroville Reservoir and 40-30-30 Index from Water Year 1981 to 2002.

| Water Year | Days in Flood Control | 40-30-30 Index |
| --- | --- | --- |
| 1981 | 0 | D |
| 1982 | 35 | W |
| 1983 | 51 | W |
| 1984 | 16 | W |
| 1985 | 0 | D |
| 1986 | 25 | W |
| 1987 | 0 | D |
| 1988 | 0 | C |
| 1989 | 0 | D |
| 1990 | 0 | C |
| 1991 | 0 | C |
| 1992 | 0 | C |
| 1993 | 8 | AN |
| 1994 | 0 | C |
| 1995 | 35 | W |
| 1996 | 22 | W |
| 1997 | 57 | W |
| 1998 | 0 | W |
| 1999 | 58 | W |
| 2000 | 0 | AN |
| 2001 | 0 | D |
| 2002 | 0 | D |

Figure A.  Total Feather River Releases form 10/1/1980 to 9/30/2002

# Natomas Releases

Natomas flood releases occur after storage has entered into the flood control reservation and releases are to be maintained between 20,000 and 115,000 cfs when inflows are increasing.  Table 3. shows the number of days that Folsom was encroached and Natomas was releasing between 20,000 and 115,000 cfs to the river in water years 1978 to 2002.  Figure 3. shows the daily average release from Natomas.

Table 3. Days in Flood Control for Folsom and 40-30-30 Index from Water Year 1978 to 2002

| Water Year | Days in Flood Control | 40-30-30 Index |
| --- | --- | --- |
| 1978 | 0 | AN |
| 1979 | 0 | BN |
| 1980 | 14 | AN |
| 1981 | 0 | D |
| 1982 | 23 | W |
| 1983 | 19 | W |
| 1984 | 15 | W |
| 1985 | 0 | D |
| 1986 | 12 | W |
| 1987 | 0 | D |
| 1988 | 0 | C |
| 1989 | 1 | D |
| 1990 | 0 | C |
| 1991 | 0 | C |
| 1992 | 0 | C |
| 1993 | 0 | AN |
| 1994 | 0 | C |
| 1995 | 3 | W |
| 1996 | 4 | W |
| 1997 | 7 | W |
| 1998 | 0 | W |
| 1999 | 3 | W |
| 2000 | 4 | AN |
| 2001 | 0 | D |
| 2002 | 0 | D |

Figure 3.  Natomas Releases from 10/1/1977 to 9/30/2002

# Goodwin Releases

Flood releases from Goodwin Reservoir were classified as releases above 1500 cfs (flows above 1500 cfs cause seepage problems down stream of the reservoir) and when New Melones is encroached.  Table 4. shows the number of days that met the flood control criteria for water years 1980 to 2002.  Figure 4. shows the daily average daily release from Goodwin.

Table 4. Days in Flood Control for New Melones and 60-20-20 Index from Water Year 1980 to 2002

| Water Year | Days in Flood Control | 60-20-20 Index |
| --- | --- | --- |
| 1980 | 0 | W |
| 1981 | 0 | D |
| 1982 | 0 | W |
| 1983 | 26 | W |
| 1984 | 54 | AN |
| 1985 | 0 | D |
| 1986 | 35 | W |
| 1987 | 0 | C |
| 1988 | 0 | C |
| 1989 | 0 | C |
| 1990 | 0 | C |
| 1991 | 0 | C |
| 1992 | 0 | C |
| 1993 | 0 | W |
| 1994 | 0 | C |
| 1995 | 0 | W |
| 1996 | 43 | W |
| 1997 | 107 | W |
| 1998 | 8 | W |
| 1999 | 56 | AN |
| 2000 | 26 | AN |
| 2001 | 0 | D |
| 2002 | 0 | D |

Figure 4.  Goodwin Releases from 10/1/1979 to 9/30/2002

2)	What is the frequency of releases within and between years that have the potential to scour salmon or steelhead redds and injure eggs or sac-fry in the gravel?  These flows would be those above the bedload mobilization point for each river in the project description.

High flows, such as those released from dams to draw down storage for flood control during heavy runoff periods, have the potential to scour salmon and steelhead redds and injure eggs or sac-fry in the gravel.  These same flows are important for maintaining rearing habitat and quality spawning gravel.  I used river specific geomorphic studies that evaluated the bedload mobilization flow and based future probability of occurrence of flow releases exceeding the bedload mobilization flow on the historic hydrograph since the respective dam was constructed.  This is a conservative analysis because flow stability recommendations from fishery agencies now result flood control releases being made by smaller intensity releases over a longer duration than occurred in the past???

# Sacramento River

Buer (1980) conducted bedload movement experiments by burying a 50 gallon drum in a riffle below Redding.  Gravel up to three inches in diameter began to accumulate in the barrel at about 25,000 cfs, indicating initiation of surface transport.  Painted rocks moved 200 to 300 feet down the riffle at 25,000 cfs.  Flows of 40,000 to 50,000 cfs would likely be required to move enough bedload to scour redds (Koll Buer, pers. comm.).  The coarse riffles (small boulders and large cobbles), are probably armored from release of sediment-free flows from Shasta Dam. These armored riffles appear not to change and thus probably remain immobile even at flows exceeding 100,000 cfs (Calfed 2000).   A bed mobility model was applied to four of the Army Corps of Engineers Comprehensive Study cross sections as another bed mobility estimate to compare to the empirical bed mobility observations.  The bed mobility model suggests bed mobility thresholds between 15,000 cfs and 25,000 cfs between River Mile 169 and 187 although the model is not considered appropriate for the Sacramento River (Calfed 2000).

Probability of occurrence for a release exceeding 25,000 cfs at Keswick Dam are approximately 50% each year and flows in the 40 – 50,000 cfs range occur in about 30 – 40% of years (figure 5-x).  On the Sacramento River, the 2-year return interval flood has been reduced from 119,000 cfs to 79,000 cfs since construction of Shasta Dam (as measured at Red Bluff, figure 5-xxx).

# Clear Creek

Sampling was conducted in Clear Creek at the USGS Clear Creek near Igo gauge during high flows in January and February 1998 to estimate a flow threshold that initiated coarse sediment transport (McBain & Trush and Matthews 1999).  Sampling bedload movement during a 2,600 cfs flow showed that mainly sand was being transported.  During a 3,200 cfs flow medium gravels were being transported.  Particles slightly greater than 32 mm were being transported by the 3,200 cfs (D84 = 7.5 mm) flow while no particles larger than 11 mm were sampled during the 2,600 cfs flow (D84 = 1.8 mm).  Their initial estimate for a coarse sediment transport initiation threshold is in the 3,000 to 4,000 cfs range.  Marked rock experiments at Reading Bar, the first alluvial reach out of the Clear Creek canyon, suggest that large gravels and cobbles (D84) are not significantly mobilized by a 2,900 cfs flow.

The majority of post Whiskeytown Dam floods are produced from tributaries downstream of Whiskeytown Dam, but floods larger than about 3,000 cfs are caused by uncontrolled spillway releases from Whiskeytown Dam, as happened in WY 1983 (19,200 cfs, the largest post-regulation flood), 1997 (15,900 cfs), and 1998 (12,900 cfs) floods.  These flows are the result of heavy runoff from the upper Clear Creek watershed and not affected by Reclamation water release operations.  Reclamation does not make releases in Clear Creek that exceed the bedload mobilization point unless recommended by fishery agencies for the benefit of fish.  A probability of exceedance plot for Whiskeytown Dam is in Figure 5-xx.  Instantaneous flows of 3,000 cfs occur on average about once every two years and flows of 4,000 cfs occur about once every three years (Figure 5-xx).  One day average flows of 3,000 cfs occur about once every five years.

Figure 5-x.  Yearly probability of exceedence for releases from Keswick Dam on the Sacramento River.

Figure 5-xx.  Clear Creek near Igo (Station 11-372000) flood frequency analysis of annual maximum, 1-day average, and 3-day average flood series for post-dam (1964 – 1997) data.

Figure 5-xx.  Yearly probability of exceedence for releases from Whiskeytown Dam on Clear Creek.

Figure 5-xxx.  Empirical flood frequency plots for the Sacramento River at Red Bluff (Bend Bridge gauge) for pre- and post-Shasta periods, and downstream at Colusa for the post-Shasta period. The reduced peak flows at Colusa reflect diversions into the Butte Basin between the two gauges. Data from U.S. Geological Survey internet site (www.usgs.gov), Red Bluff (Bend Bridge) and Colusa gauges.  Chart from Calfed (2000).

# American River

Ayres Associates (2001) used a two-dimensional model of the lower American River constructed from two foot topography to determine at what flows spawning beds would be mobilized.  Their modeling results indicated that the spawning bed materials are moving for flows of 50,000 cfs or greater.  There appeared to be minimal movement for flows as low as 30,000 cfs, although some movement may occur for flows between 30,000 and 50,000 cfs.  Shear stress conditions tend to be highest upstream of Goethe Park, where the majority of salmon and steelhead spawning occurs.

Flood frequency analysis for the American River at Fair Oaks Gauge shows that on average flows will exceed 30,000 cfs about once every four years and exceed 50,000 cfs about once every five years (Figure 5-xx).  Fair Oaks gauge flows result almost entirely from Folsom and Nimbus releases.

Figure 5-xx.  Flood frequency analysis for the American River at Fair Oaks Gauge (U.S. Army Corps of Engineers 1999).

# Stanislaus River

Kondolf et al (2001) estimated bedload mobilization flows in the Stanislaus River to be around 5,000 to 8,000 cfs to mobilize the D50 of the  channel bed material.  Flows necessary to mobilize the bed increased downstream from a minimal 280 cfs near Goodwin Dam to about 5,800 cfs at Oakdale Recreation Area.

Before construction of New Melones Dam, a bed mobilizing flow of 5,000 to 8,000 cfs was equivalent to a 1.5 to 1.8 year return interval flow.  On the post dam curve, 5000 cfs is approximately a 5-year return interval flow, and 8,000 cfs exceeds all flows within the 21 year study period, 1979 - 1999 (max flow = 7,350 cfs on 1/3/97).  The probability of occurrence for a daily average flow exceeding 5,330 cfs (the pre-dam bankfull discharge) is 0.01, or one year in a hundred.  Figure 5-xx shows the yearly exceedance probability for Goodwin Dam releases.

Figure 5-x.  Exceedance probability for yearly Goodwin Dam releases.

# Feather River

DWR is currently studying sediment transport as part of the FERC re-licensing effort for the Oroville facilities.  Using computer models such as Feluvial 12 DWR hopes to better quantify the range of flows and locations when and where bedload mobilization occurs.  This work is being done in coordination with NOAA fisheries.  Of note, the last significant bedload movement occurred in 1997.  Since then flows have not exceeded 25,000 cfs.

3)	What is the frequency for flow fluctuations within and between years from controlled releases that have the potential to dewater salmon and/or steelhead redds or isolate and strand juvenile salmonids below project reservoirs?

# American River

Snider et al (2001) evaluated flow fluctuations relative to stranding in the American River and made the following recommendations for operations of the Folsom project.

- Ramping rates should not exceed 100 cfs per hour when flows are < 4,000 cfs;

- Flow increases to 4,000 cfs or more should be avoided during critical periods (January through July for young of the year salmon and steelhead and October through March for yearling steelhead and non-natal rearing winter-run chinook salmon) unless they can be maintained throughout the entire period…..Need to get a frequency of occurrence for flow increases that go to 4,000 and then drop back down throughout the year (except for August and September but essentially all year) ; and

- Flow fluctuations that decrease flow below 2,500 cfs during critical spawning periods should be precluded:  October – December for chinook salmon and December – May for steelhead.  They define flow fluctuations as unnatural rapid changes in stream flow or stage over short periods resulting from operational activities of dams and diversions.

The shallowest salmon redds observed prior to any flow changes were 5” deep (Hannon, field observations 2002) and the shallowest steelhead redds observed were over 7” deep (Hannon and Healey 2002).  Steelhead could likely spawn in water as shallow as chinook so a conservative analysis is based on water depth reductions of 5” that could drop the water level to even with the top of the shallowest redds.  The eggs are generally buried at least 5” …..reference……under the gravel so the shallowest eggs would not become dewatered until water drops at least 10” but fry emergence could be prevented if no water is over the surface of the redd.  Based on cross sections measured in 1998 by the Fish and Wildlife Service, flow changes of 100 cfs generally change the water depth by about 1 inch in a flow range of 1,000 to 3,000 cfs and by about 0.5 inch in a flow range from about 3,000 to 11,000 cfs.  Therefore, when flows are 3,000 cfs or lower flow drops of 500 cfs or more can begin to dewater redds.  When flow is over 4,000 cfs flow drops of 1,000 cfs or more can begin to dewater redds.  Need a frequency of occurrence for these flow drops between November 1 and June 1….this is the period when chinook and steelhead eggs are in the gravel.

Clear Creek….

Table 5.xx shows the stage discharge relationship in Clear Creek at Igo.  If we use the 5” redd depth as the threshold for redd dewatering then a flow drop of 100 cfs in the 100 to 300 cfs range could start to dewater the shallowest redds.  A flow drop of 150 cfs in the 300 to 800 cfs range could start to dewater redds and a flow drop of 300 cfs between 800 and 1,800 cfs could start to dewater redds….need frequency of occurrence for this.  Flows over 500 cfs in Clear Creek are the result of uncontrolled runoff or pulse flows prescribed through collaboration with fishery agencies for the benefit of fish and habitat.

Table 5.xx.  Stage discharge relationship for the Clear Creek at Igo USGS gauge, Station 11-372000.

| Stage, inches | Discharge, cfs |
| --- | --- |
| 33.12 | 101 |
| 38.52 | 200 |
| 42.72 | 301 |
| 46.2 | 400 |
| 49.32 | 501 |
| 52.2 | 602 |
| 54.72 | 702 |
| 57 | 803 |
| 59.16 | 903 |
| 61.08 | 1000 |

Sacramento River….

Based on the Sacramento River at Bend Bridge gauge, drops in flow of approximately 800 cfs in the low end of the flow range up to about 20,000 cfs have the potential to start to dry up the shallowest redds 5” deep (Table 5.xxx).  Areas of the river away from stream gauges where there is not as much confinement and more spawning activity probably experience less change in stage for a given flow change but the data was not available to evaluate other locations.   Need frequency of occurrence.

Table 5.xxx.  Stage discharge relationship in the Sacramento River at Bend Bridge, gauge 11377100.

| Stage, inches | Discharge, cfs |
| --- | --- |
| 8 | 4190 |
| 10 | 4500 |
| 12 | 5020 |
| 15 | 5490 |
| 18 | 5990 |
| 21 | 6490 |
| 24 | 6990 |
| 27 | 7490 |
| 31 | 7990 |
| 34 | 8500 |
| 38 | 9000 |
| 41 | 9510 |
| 45 | 10000 |
| 48 | 10500 |
| 52 | 11000 |
| 55 | 11500 |
| 59 | 12000 |
| 62 | 12500 |
| 65 | 13000 |
| 68 | 13500 |
| 71 | 14000 |
| 74 | 14500 |
| 78 | 15000 |
| 81 | 15500 |
| 84 | 16000 |
| 87 | 16500 |
| 90 | 17000 |
| 92 | 17500 |
| 95 | 18000 |
| 98 | 18500 |
| 101 | 19000 |
| 103 | 19500 |
| 106 | 20000 |
| 110 | 21000 |
| 114 | 22000 |
| 118 | 23000 |
| 122 | 24000 |
| 126 | 25000 |
| 129 | 26000 |
| 133 | 27000 |
| 137 | 28000 |
| 140 | 29000 |
| 144 | 30000 |

Stanislaus River….

Based on the Stanislaus River at Ripon gauge, drops in flow of approximately 50 cfs in the flow range of 100 to 300 cfs have the potential to start to dry up the shallowest redds five inches deep (Table 5.xxx).  Although the Ripon gauge is downstream of spawning areas, the channel morphology at the gauging station is similar to that through much of the spawning area so the stage discharge relationship should be similar.  Drops in flow of 100 cfs in the flow range of about 300 to 1,000 cfs will cause a 5 inch drop in water surface elevation.  Drops in flow of about 175 cfs in the flow range of 1,000 to 2000 cfs will cause about a five inch drop in water level.

Need an analysis of the frequency of occurrence for these flow drops here between November 1 and May 30.

Table 5.xxx.  Stage discharge relationship in the Stanislaus River at Ripon, gauge 11303000…..would be good to get the Orange Blossom gauge rating from dwr.

| Stage, inches - 440 | Discharge, cfs |
| --- | --- |
| 3 | 100 |
| 5 | 125 |
| 8 | 150 |
| 10 | 174 |
| 13 | 200 |
| 17 | 251 |
| 21 | 300 |
| 24 | 350 |
| 27 | 400 |
| 32 | 501 |
| 37 | 601 |
| 43 | 700 |
| 49 | 800 |
| 54 | 900 |
| 58 | 1000 |
| 67 | 1200 |
| 76 | 1400 |
| 84 | 1600 |
| 92 | 1800 |
| 100 | 2000 |
| 120 | 2500 |
| 139 | 3000 |
| 175 | 4000 |
| 199 | 5000 |
| 215 | 6000 |

# Feather River

Controlled releases may change for many reasons at any time.  Flow rates in the low-flow channel rarely change except during flood events and are typically just over 600 cfs.  Studies of dewatering in the Feather River below the Afterbay outlet are ongoing.  Studies results to date suggest some dewatering may occur to salmon redds in the high flow section of the river (downstream from the Afterbay outlet) when flows steadily over 2000 cfs drop below 1700 cfs during the months October through January.  Over the past 23 years such dewatering conditions occurred eight times.

For more information on stranding of juveniles see DWR’s report to National Marine Fisheries Service, 2003.  For this narrative I’m assuming that rearing juveniles are susceptible to stranding in the Feather River below the Afterbay outlet when the river decreases by more than half over seven days with flows fluctuating between 1000 and 8000 cfs.  Since 1980 such flow fluctuations have occurred sixteen times in the January through June rearing season.

4)	What is the frequency of controlled flow decreases ( i.e. non-flood control), that occur due to sudden changes in operations (i.e., meeting water quality standards) and the predicted season of occurrence?

Release logs from 1995 to present were used to analyze flow decreases.  The time period was chosen because the operations since 1995 more accurately reflect the decreases that would occur due to changes in operations in the next OCAP.  The following sections discuss the decreases in Reclamations Keswick, Whiskeytown, Nimbus and Goodwin reservoirs.

# Keswick Reservoir

Figure X shows the percent of total decreases by month since May 1995.  The majority of the decreases occur between Aug and Oct due, generally, to either fall ramp down or because of improving water temperature in the river.  The majority of decreases from Nov to Jan are decreases to conserve water after increases for the Delta or to maintain an adequate dilution with Spring Creek Debris dam.  Mar to May decreases follow increases for Delta needs, improving water temperatures, or after maintaining downstream flows.

Figure X. Percent of Total Keswick Operational Decreases (non-flood control) since May 1995 by month

# Whiskeytown Reservoir

The percent of total decreases in Whiskeytown since 1995 by month are in Figure X.  Decreases from Whiskeytown are mainly due to improving water temperatures, removal of Setzer Dam, decreasing flow requirements, and recommendations from Fish & Wildlife Service due to B2 costs or CVPIA.

Figure X. Percent of Total Whiskeytown Operational Decreases (non-flood control) since May 1995 v

# Nimbus Reservoir

Figure X shows the percent of total decreases by month since 1995 for Nimbus.  The Jan to Apr decreases are mainly for conservation of storage after flood events.  The May to Sep decreases are a mixture of both decreases for conservation and after a release to help meet delta requirements.

Figure X. Percent of Total Nimbus Operational Decreases (non-flood control) since May 1995 by month

# Goodwin Reservoir

The Figure X shows that decreases in releases from Goodwin happen generally between Apr to Oct.  The Oct decreases are due to conserving water after the fall attraction flows.  The decreases from Apr to Sep are generally due to conserving storage while water quality at either Ripon or Vernalis are improving.

Figure X. Percent of Total Nimbus Operational Decreases (non-flood control) since May 1995 by month

# Feather River

Total Feather River Releases were examined from water year 1981 to water year 2002.  Total Flow decreases were separated into flood control related decreases and non-flood controlled decreases.  Flood control related decreases were defined as any decreases made within 2 weeks of a flood control release as defined in Question 1.

The monthly probability of a non-flood control Feather River decrease was plotted using the data from 1981-2002.  The plot shows that November is the least likely month for a non-flood related flow decrease.   Decreases in the other months could be partially attributed to the SWP response to temperature releases in CVP upstream reservoirs.  The relatively high October decreases are due to reductions to meet the 2500 cfs Feather River target from Oct 15 to Nov 30.

5)	Describe and explain the biological rational for planned instream releases downstream of project dams included in the long term OCAP.  Include an incremental analysis of various flows between lethal and optimum for all life stages of salmon (i.e. optimum flows for steelhead over summer rearing, or spring-run Chinook spawning).  Cite the basis for determination (i.e., previous IFIM study or habitat studies).  In previous BA’s, analysis of the suitability of instream flows were based on using fall-run Chinook salmon criteria and may not be adequate for steelhead or spring-run Chinook salmon. Please include an analysis of the suitability of proposed flow rates for steelhead, spring-run Chinook and winter-run Chinook salmon.  (Note: recent Feather River flow information could be provided in a supplemental after this year’s studies are completed)

The temperature modeling results along with the chinook mortality model will be used to evaluate effects of water temperature on incubating eggs in each of the tributaries.  We may be able to produce an incremental analysis of effects of various flows on temperature related mortality by running the temperature model to predict temperature at a point in each river using a single release temperature versus a range release flows.  Resultant temperatures could be compared to temperature requirements of rearing steelhead and chinook.  If rearing area flows or migratory flows are needed I have not found anything to use for an incremental analysis other than the fact that no water = 100% mortality and as we increase flows above that mortality will drop.

Table 5-xx shows the relationship between water temperature and mortality of chinook eggs and pre-emergent fry compiled from a variety of studies.

| Table 5-xx Relationship Between Water Temperature and Mortality of Chinook Salmon Eggs and Pre-Emergent Fry |
| --- |
| Water Temperature ((F)a | Egg Mortalityb | Instantaneous Daily Mortality Rate (%) | Pre-Emergent Fry Mortalityb | Instantaneous Daily Mortality Rate (%) |
| 41-56 | Thermal optimum | 0 | Thermal optimum | 0 |
| 57 | 8% @ 24d | 0.35 | Thermal optimum | 0 |
| 58 | 15% @ 22d | 0.74 | Thermal optimum | 0 |
| 59 | 25% @ 20d | 1.40 | 10% @ 14d | 0.75 |
| 60 | 50% @ 12d | 5.80 | 25% @ 14d | 2.05 |
| 61 | 80% @ 15d | 10.70 | 50% @ 14d | 4.95 |
| 62 | 100% @12d | 38.40 | 75% @ 14d | 9.90 |
| 63 | 100% @11d | 41.90 | 100% @ 14d | 32.89 |
| 64 | 100% @ 7d | 65.80 | 100% @10dc | 46.05 |
| aThis mortality schedule was compiled from a variety of studies each using different levels of precision in temperature measurement the lowest of which was whole degrees Fahrenheit (+0.5oF). Therefore, the level of precision for temperature inputs to this model is limited to whole degrees Fahrenheit. bThese mortality schedules were developed by the U.S. Fish and Wildlife Service and California Department of Fish and Game for use in evaluation of Shasta Dam temperature control alternatives in June 1990. cThis value was estimated similarly to the preceding values but was not included in the biological assumptions for Shasta outflow temperature control FES (USBR, 1991b). |

The following are IFIM study results for spawning habitat.

# Sacramento River

U.S. Fish and Wildlife Service (2003) developed spawning flow-habitat relationships for steelhead spawning habitat in the Sacramento River below Keswick Dam using the Physical Habitat Simulation (PHABSIM) component of the instream flow incremental methodology (IFIM).  Relationships were developed by cross section and by stream segments but were not aggregated into river-wide flow-habitat relationships.

Steelhead spawning wetted usable area peaked at 3,250 cfs in the reach upstream of the ACID Diversion Dam both when the dam boards are out and when the boards are in.  Between ACID Dam and Cow Creek spawning area also peaked at 3,250 cfs.  In the lower reach, from Cow Creek to Battle Creek, spawning area peaked at about 13,000 cfs but did not vary significantly in a flow range between about 6,000 and 14,000 cfs.

The minimum Sacramento River flow allowed is 3,250 cfs.  This flow level provides adequate physical habitat to meet the needs of all steelhead life stages in the Sacramento River.  Flows during the summer greatly exceed this amount to meet temperature requirements for winter-run.  The winter-run temperature requirements result in water temperatures suitable for year-round rearing of steelhead in the upper Sacramento River.

# Clear Creek

Denton (1986) used the IFIM to estimate optimal Clear Creek flows for salmon and steelhead.  The resultant estimate of optimal flows from the IFIM study is shown in figure 4-x.  Summer-rearing habitat resulting from high water temperatures appeared to be the limiting factor for steelhead.  Optimal steelhead flows in the upstream (above the former Saeltzer Dam site) reach were 87 cfs for spawning and 112 cfs for juvenile rearing.  Optimum flows for steelhead in the reach below Saeltzer Dam were predicted to be 250 cfs in all months except April when they drop to 225 cfs and May 1 – May 15 when they are 150 cfs.  Denton (1986) recommended that tributary streamflows occurring below Whiskeytown Dam should be included in computing the additional releases required from Whiskeytown Dam to meet the total recommended fishery flow needs.

# American River

USFWS (1997) measured 21 cross sections of the American River in high density chinook spawning areas. They estimated the flows at which the greatest usable spawning area would be available to steelhead and chinook based on measurements of water velocity, water depth, and substrate size from steelhead and chinook redds in the American River.  There was low variability in weighted usable spawning area (WUA) throughout the range of flows analyzed (1,000 to 6,000 cfs).   Table 4-7 shows the average of the weighted usable spawning area from the 21 cross sections expressed as 1,000 square feet of spawning area per 1,000 feet of stream. WUA for steelhead peaked at a flow of 2,400 cfs.  All flows from 1,000 cfs to 4,000 cfs provided at least 84% of the maximum WUA.

Table 3-xx  Average weighted usable spawning area (expressed as 1,000 square feet of spawning area per 1,000 feet of stream) from 21 cross sections measured in 1995 in high density chinook spawning areas. Summarized from USFWS 1997.

| Nimbus Release (cfs) | Steelhead Average WUA | Chinook Average WUA |
| --- | --- | --- |
| 1000 | 31 | 62 |
| 1200 | 33 | 71 |
| 1400 | 34 | 78 |
| 1600 | 35 | 82 |
| 1800 | 36 | 84 |
| 2000 | 36 | 83 |
| 2200 | 36 | 81 |
| 2400 | 37 | 78 |
| 2600 | 36 | 74 |
| 2800 | 36 | 69 |
| 3000 | 36 | 65 |
| 3200 | 36 | 60 |
| 3400 | 35 | 56 |
| 3600 | 34 | 52 |
| 3800 | 32 | 48 |
| 4000 | 31 | 45 |
| 4200 | 29 | 42 |
| 4400 | 27 | 38 |
| 4600 | 26 | 36 |
| 4800 | 24 | 33 |
| 5000 | 23 | 31 |
| 5200 | 22 | 28 |
| 5400 | 21 | 26 |
| 5600 | 20 | 25 |
| 5800 | 19 | 23 |
| 6000 | 19 | 21 |

Snider et al (2001) evaluated effects of flow fluctuations in the American River on steelhead and salmon.  They defined flow fluctuations as unnatural rapid changes in stream flow or stage over short periods resulting from operational activities of dams and diversions.  They recommended ramping flows in the American River of 100 cfs per hour or less at flows less than 4,000 cfs to reduce stranding of steelhead caused by rapid dewatering of habitat.  They further recommended avoiding flow increases to 4,000 cfs or more during critical rearing periods.  These are January through July for young of year salmon and steelhead, and October through March for yearling steelhead and non-natal rearing winter-run chinook salmon unless the higher flows can be maintained throughout the entire period.  For the maintenance of sufficient spawning habitat and to keep water flowing through redds they recommended precluding flow fluctuations that decrease flow below 2,500 cfs during critical spawning periods (December through May).

Ayres Associates (2001) used detailed topography of the river to model sediment mobilization at various flows in the American River. They found that at 115,000 cfs (the highest flow modeled) particles up to 70 mm median diameter would be moved in the high density spawning areas around Sailor Bar and Sunrise Avenue. Preferred spawning gravel size is 50 - 125 mm (2-5 inches) in diameter.

Snider et al (2001) produced survival indices for chinook salmon based on number of redds versus the population estimate of outmigrating juveniles over seven years of monitoring.  They found that high flows in January had the largest effect on survival according to the following equation:  Survival = 11,244.5*(January maximum flow, cfs)-0.278684.  The higher the flow in January the lower the survival index. January is the time period with the greatest number of chinook eggs in the gravel so supposedly the high flows are reducing survival of incubating eggs by scouring or suffocating the eggs and alevins in redds.  Because steelhead spawn in similar habitat and require similar incubation conditions high flows may effect incubating steelhead eggs in a similar manner.  Few attempts have been made to estimate steelhead spawning population or juvenile populations so no such relationship can be examined for steelhead.

Monitoring has shown that juvenile steelhead numbers in the river decrease throughout the summer such that the available rearing habitat is not fully seeded with fish.  Therefore the rearing population in the river is not likely limited by density dependent factors.  More likely water temperature and potentially predator fish species such as striped bass limit the rearing population of steelhead in the American River.  Flows of about 1,500 cfs or greater have sufficient thermal mass to maintain much of the water temperature benefits of cool Folsom releases downstream to Watt Avenue while maintaining a sufficient cold water pool to last through summer and fall.

# Feather River

Tom Payne flow study results…….

# Stanislaus River

Aceituno (1993) applied the instream flow incremental methodology to the Stanislaus River between Riverbank and Goodwin Dam (24 river miles) to help to determine instream flow needs for chinook salmon and steelhead. Table 2-1 gives the resulting instream flow recommendations for rainbow and steelhead based on PHABSIM results.  Macrohabitat conditions such as water quality, temperature, and the value of outmigration, attraction, and channel maintenance flows were not included in the analysis.

| Table 2-1 Instream flows that would provide the maximum weighted usable area of habitat for rainbow trout and steelhead trout in the Stanislaus River between Goodwin Dam and Riverbank, California (Aceituno 1993). |
| --- |
| Life stage | Instream flow (cfs) |  |
|  | for rainbow trout | for steelhead |
| Spawning | 100 | 200 |
| Fry | 50 | 50 |
| Juvenile | 150 | 150 |
| Adult | 400 | 500 |

# Clear Creek

Denton (1986) used the IFIM to estimate optimal Clear Creek flows for salmon and steelhead.  The resultant estimate of optimal flows from the IFIM study is shown in figure 4-x.  The timing of these flows was based on the fall run chinook life cycle, but the recommended steelhead flows would provide the needed flows for spring run, except potentially in April and May when an extra 25 cfs would bring the flows up to the salmon recommendation.  The recommended spawner attraction flow releases shown in October and November could be provided around April and May for spring run.

Although the optimum flows that were recommended for salmon (fall run) of 250 cfs may provide a maximum amount of suitable spring run spawning and rearing habitat, because the number of spring run in Clear Creek is low the population does not appear to be currently habitat limited as long as temperatures are suitable.  The section of Clear Creek from the mouth to the former Saeltzer Dam is fall and late-fall chinook habitat, while the Clear Creek Road Bridge to Whiskeytown Dam reach is the section of creek more suitable for spring-run chinook because temperatures are better in that upstream reach in the summer.  The IFIM study showed higher flow needs in the downstream habitat than in the upstream habitat.  Optimal flows for salmon in the upstream reach where spring run are located were 62 cfs for spawning and 75 cfs for rearing from the IFIM study (Denton 1986).  Optimal steelhead flows in the same upstream reach were 87 cfs for spawning and 112 cfs for juvenile rearing.

# Sacramento River

U.S. Fish and Wildlife Service (2003) developed spawning flow-habitat relationships for winter, fall, and late fall chinook salmon and steelhead spawning habitat in the Sacramento River below Keswick Dam using the Physical Habitat Simulation (PHABSIM) component of the instream flow incremental methodology (IFIM).  Relationships were developed by cross section and by stream segments but were not aggregated into river-wide flow-habitat relationships.

Winter run chinook salmon spawning usable area peaked at around 10,000 cfs in the upstream reach above ACID Dam when the dam boards are in;  with the boards out the peak was around 4,000 – 5,000 cfs.  In the next reach downstream (ACID Dam to Cow Creek) habitat peaked at 8,000 – 9,000 cfs.  In the lower reach (Cow Creek to Battle Creek) spawning habitat peaked at around 4,000 cfs but had low variability in wetted usable spawning habitat area in the flow range analyzed (3,250 – 30,000 cfs).  The highest density redd counts for winter-run occur in the middle reach, although since the ACID fish ladder was built there has been a substantial increase in spawning upstream of the dam (Killam 2002).

Fall-run and late-fall run had different wetted usable spawning area values but the flow versus habitat relationship was about the same for the two runs.  Upstream of the ACID Dam, spawning habitat peaked at 3,250 cfs with the dam boards out and at about 6,000 cfs with the boards in.  Between ACID and Cow Creek spawning habitat peaked at around 4,000 cfs.  Between Cow Creek and Battle Creek habitat peaked at about 3,500 cfs.  The highest density redd counts for fall and late fall-run occur in the middle reach.

6)	Describe the intended operation of Red Bluff Diversion Dam(RBDD) for the term of the proposed long term OCAP.  An EIS/EIR has been prepared and several alternatives have been proposed.  Reclamation needs to describe the preferred alternative to be used in this consultation.  This is necessary to conduct an analysis of impacts to steelhead, winter-run Chinook and spring-run Chinook salmon.

Reclamation’s preferred alternative for the consultation is the No Action Alternative in the Fish Passage Improvement Project at the Red Bluff Diversion Dam Draft EIR/EIS (USBR-TCCA, 2002).  This alternative uses the existing operations of the RBDD and is the operation to be used in the foreseeable future.  The operation outlined in the No Action Alternative is:

- RBDD Operation: Gates in 4-month (May 15 through September 15).

- Continue operating the Research Pumping Plant and add a fourth pump.

- Eliminate Stony Creek diversions (because of a lack of feasible options for constructing a fish screen on the Constant Head Orifice)

7)	Describe how the Tracy Fish Collection Facility (TFCF) will be operated. What is the schedule for improvements at the TFCF to bring the facility into compliance with current NMFS screening criteria?  Include a proposed schedule for dive inspections and fish efficiency testing along with proposed operations and maintenance of facility fish screens.  Describe how repairs will be made, if determined necessary, and how the TFCF will be operated during these repairs. Describe how the TFCF will be operated during construction of the new Tracy Fish Test Facility (TFTF) and in the event that the TFTF is not constructed.  Reclamation selected the preferred alternative (Modified Site A) on November 27, 2001, for Phase One of the new TFTF.  The proposed action will change operations as previously described in project descriptions for existing biological opinions.  A detailed description of the proposed monitoring plan and schedule for construction of the TFTF should be completed and included in the BA.

The Tracy Fish Collection Facility (TFCF) will continue to be operated as per the original design criteria and the most recent Biological Opinions, SWRQB Decisions  D-1485 & D-1641, and Tracy Direct Loss Agreement, until such a time as the biological opinions, or Decisions, or Direct Loss Agreement are modified or superceded.

There is no current schedule to bring the TFCF into compliance with current NMFS screening criteria. There are differences of opinion currently between Reclamation and NMFS over the applicability, feasibility, and practicality of attempting to implement current NMFS screening criteria in the south Delta environment as it relates to fish salvage. There are plans to continue research efforts, however, related to improving or replacing the existing TFCF as per CVPIA Section 3406(b)(4). There is no current timetable on when these improvements will be implemented. Some improvements have already been implemented, including purchase/design of new fish haul trucks, implementation of a predator removal program, and coating of the recessed collection tanks.

There currently is no long term schedule for dive inspections, however, there is a dive inspection scheduled for May, 2003 to inspect the bypass transition boxes. TFCF efficiency testing is an on-going effort involving many aspects of the TFCF, including pre-screening losses, louver efficiencies, collection, handling, and transportation. Notice of intent to perform efficiency testing as well as review of testing protocol is distributed and reviewed prior to commencement of testing effort. Testing data is made public after testing has been completed and reviewed. Operations and Maintenance is scheduled on a regular basis utilizing the services of on-site staff, the San Luis & Delta Mendota Water Authority, and contract personnel. The trash rack screens and primary louver screens are normally cleaned 2 – 3 times per day or as often as needed depending on debris load. On-site personnel visually inspect the trash rack and primary louver screens on a regular basis and there is also a backup alarm system in case a differential of 3 feet or greater is detected.  The secondary louver screens do not collect debris at the same rate as the trash rack screens or primary louver screens and as such are cleaned only about once per day or as needed depending on debris load. The secondary louver screens are visual inspected on a regular basis. There is no backup alarm system for these screens. Preventive maintenance is handled by SL&DMWA personnel as per an established schedule.

Routine and breakdown maintenance is normally handled by either on-site personnel, SL&DMWA personnel, or contractor personnel, or a combination thereof. The TFCF will continue to be operated as best as possible to meet current operating criteria during repairs. However, if this can not be obtained and the repair exceeds two hours, then proper coordination and consultation will occur between Reclamation and the regulatory agencies to determine what changes in operation at the Tracy Pumping Plant (TPP) should occur, if any.

The TFCF will continue to be operated as per current operating criteria during construction of the Tracy Fish Test Facility (TFTF), if the TFTF is constructed. In the event that an action occurs during construction of the TFTF that adversely effects operation of the TFCF for greater than two hours such that the TFCF is not able to meet existing operations criteria, then immediate coordination and consultation will occur between Reclamation and the regulatory agencies to determine what changes in operation at the TPP should occur, if any. If the TFTF is not constructed, then the TFCF will continue to operate as per existing criteria until that criteria is changed (see first paragraph above).

In he event that the TFTF is decided to be constructed, a detailed monitoring plan and schedule for construction will be completed and included in the EA/IS, or in an amendment to the EA/IS. No final decision has been made at this time as to whether or not to construct a TFTF, and if so to what scale and components.

Current estimates for daily loss rate for juvenile steelhead at the TFCF is similar to that of Chinook salmon (i.e. 15% pre-screen loss, 25% louver losses, and 4% handling & trucking losses). As additional studies are conducted related to juvenile steelhead at the TFCF and information gathered related to their loss rate, then the loss rate will be adjusted upon coordination and consultation with the regulatory agencies.

8)	Describe and explain how Reclamation’s proposed special studies, included under the Central Valley Improvement Act (CVPIA) Tracy Fish Facilities Improvement Program, are expected to affect planned operations proposed under the long term OCAP?  Are these special studies considered part of the proposed long term OCAP?  If they are, describe the methods used to determine a loss estimator of steelhead, spring-run and winter-run Chinook salmon associated with these special studies along with anticipated direct and/or incidental take of listed salmonids for the duration of these studies.

It is not anticipated that Reclamation’s proposed special studies, including those under CVPIA TFFIP, are expected to significantly affect planned operations proposed under the long term OCAP. If anticipated impacts to operations arise as a result of the special studies, then these impacts will be delineated in the proposed study plans and coordinated with Reclamation’s Central Valley Operations (CVO) Office and the appropriate regulatory agencies.

These special studies are part of the long term OCAP and should be covered either under ESA Section 7 consultation or Section 10 permitting. As such, until the special studies are developed, it is difficult, if not impossible, to determine a loss estimator for steelhead and spring-run and winter-run Chinook salmon associated with these studies, along with anticipated direct and/or incidental take of listed salmonids for the duration of these studies. This is probably best handled during the Section 10 permitting process as requested by NMFS.

9)	Discuss the effects to salmonids of increasing DWR’s diversions through the North Bay Aqueduct (NBA) at Barker Slough (as proposed in the North Bay Settlement Agreement). These effects should be addressed in relation to increased entrainment at the NBA pumps and false attraction of adults to the point(s) where this water re-enters the Delta.

The North Bay Aqueduct serves Solano and Napa counties.  The effluent from these counties does not re-enter the Delta, however some effluent may eventually reach the Suisun Marsh.  The settlement agreement with the cities of Vacaville, Fairfield and Benicia may increase diversions at Barker Slough pumping plant during times of excess conditions (and balanced conditions when Term 91 is not in effect.)  However, diversions at Barker Slough will remain within the operable limitations of the positive barrier fish screens and should not increase entrainment.  Impacts to listed species should not be significantly greater than those discussed in existing biological opinions for winter-run Chinook salmon.

10)	Discuss the impacts to listed salmonids from additional “Wheeling” of 300 TAF in Dry Years through the SWP’s Harvey O. Banks Pumping Plant.  Is this included in the current CALSIM II modeling, if so describe how?  What is the expected frequency of occurrence for this action?

The Dry Year Purchase program may involve wheeling up to 300 TAF during times of drought. This wheeling will likely occur in summer months July through September and have very little impact on salmonids in the Delta. The source for the water will vary but will likely be derived from reduced agricultural usage throughout Northern and Central California. It will not likely reduce reservoir storage significantly if at all and thus not likely impact samonids migrating or rearing in the applicable streams.

11)	Describe the anticipated operations and plans for proposed permanent barriers in the South Delta in addition to the current temporary barriers, including the anticipated effects of barrier operations on Delta water elevations, Delta water quality, and fish passage with and without the permanent barriers in place.

The following discussion of barrier operations comes from the SDIP Administrative Draft EIR/EIS as they pertain to fish in the Delta.

Barrier Operations

Head of Old River Fish Control Barrier

The head of Old River barrier would be operated from April 14 to June 1 (if requested by the fish agencies) and September 15 to November 30 (if a dissolved oxygen problem exists near the Stockton Turning Basin). This would allow for the protection of San Joaquin River fall-run salmonids during both spring and fall periods. Additional operation periods may be requested by fish agencies in response to the presence of fish or anoxia conditions in the San Joaquin River.

In the fall, the barrier would be operated from October through November of each year except during periods of high San Joaquin River flows. Operations during the fall are focused on improving the dissolved oxygen levels along the portion of the San Joaquin River from its confluence with the head of Old River downstream to the Port of Stockton.

In the spring, the barrier would be operated from April 16 to May of each year except during periods of high San Joaquin River flows. Operations during the spring would be focused on enhancing the survival of emigrating San Joaquin River salmon smolts by reducing the chance of exposure to the influences of project and local diversions occurring in the south Delta during these timeframes.

The exact timing of both the fall and spring operations could be modified annually, in coordination with DFG. Operations may also be modified in response to varying conditions to avoid impacts on winter-run salmon and Delta smelt. During nonoperational times of the year, the gates would remain fully raised.

Flow Control Barriers

The barriers would be operated to fulfill the commitments of DWR and Reclamation in the water level response plan. Specifically, Reclamation and DWR have committed to maintaining water levels of 0.0 foot msl in Old River near the Tracy pumping plant, and 0.0 foot msl at the west end of Grant Line Canal, and 0.5 foot msl in Middle River at Tracy Road. It is anticipated that the target level in Middle River would be lowered to 0.0 foot msl following extension of agricultural diversions.

Proposed barrier operations (closing the radial gates of the proposed structures) would require forecasting of water levels in south Delta channels and operating the barriers to maintain the agreed-upon water levels. Forecasting would be performed on a weekly basis using the Delta Simulation Model 2 (DSM2), using 16 years of real tide data, and proposed diversion rates of the projects.

The DSM2 calculates hydraulic parameters for hundreds of points in Delta channels every 15 minutes. Using simulation of pumping rates, release schedules, and forecast tides, stage throughout the south Delta channels would be predicted. Where stage is predicted to be below the criteria (water level response plan), the barriers would be operated to retain stage. Once the low-tide event has passed and the stage can be preserved through natural means, the barriers would be opened to enhance flow through these channels.

Based on these factors, it is expected that barriers would need to be closed approximately 2 hours before the low-tide event and for about 2 hours after the low-tide event has passed. Actual operations vary slightly from this estimate but would be implemented with an eye toward maintaining fish passage, water quality, and stage.

The extension of agricultural diversions in the south Delta that are currently less than –2 feet msl may lower the water level response criteria and subsequently further reduce the need to operate barriers.

The graphs on the following page shows the upstream and downstream effects of Grant Line Barrier for 10 days in Oct 1975 and Jan 1976 with Grant Line Wier Crest elevations of 1 ft msl and 0 ft msl.

The three graphs on the following page show the difference in EC for Mowery Bridge at Middle River, Tracy Road at Old River, and Tracy Road at Grant Line Canal between having the Grant Line Wier Crest elevations of 1 ft msl and 0 ft msl.

The following tables show the percent of time the barriers would be closed for each of the scenarios.

| South Delta Barrier Operations (EIR/EIS Study) |
| --- |
| 2020 Revised Fish Scenario |
| Monthly Breakdown of South Delta Ag Barrier Operations |
| Middle and Old River Full Barrier, Grant Line Special Weir (Crest Level = 0 msl, throught the year) & No Buf. Time |
| Percent Time Barrier Closed |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Middle River Ag Barrier |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 |
| Oct | 58.0 | 19.2 | 24.1 | 27.6 | 30.7 | 38.8 | 26.0 | 18.2 | 13.4 | 34.0 | 24.8 | 25.8 | 15.6 | 22.5 | 25.4 | 20.5 |
| Nov | 58.0 | 20.0 | 20.8 | 26.7 | 33.2 | 29.1 | 41.7 | 8.7 | 2.5 | 37.3 | 24.9 | 23.5 | 20.7 | 29.7 | 19.1 | 18.5 |
| Dec | 65.9 | 12.3 | 22.7 | 35.7 | 46.2 | 27.6 | 12.1 | 0.0 | 0.0 | 37.3 | 24.2 | 19.7 | 19.1 | 29.2 | 19.6 | 20.7 |
| Jan | 40.5 | 14.3 | 0.9 | 26.0 | 0.5 | 34.4 | 3.4 | 0.0 | 0.0 | 32.7 | 27.3 | 30.0 | 36.1 | 37.8 | 35.9 | 19.3 |
| Feb | 18.9 | 22.6 | 0.0 | 0.4 | 0.0 | 21.4 | 0.6 | 0.0 | 0.0 | 26.5 | 0.0 | 16.7 | 22.6 | 22.3 | 25.1 | 16.6 |
| Mar | 29.8 | 33.4 | 0.0 | 0.8 | 0.0 | 10.2 | 0.0 | 0.0 | 4.4 | 25.9 | 0.0 | 17.6 | 17.2 | 23.5 | 25.8 | 22.3 |
| Apr | 23.2 | 34.1 | 3.1 | 26.7 | 27.5 | 25.1 | 0.0 | 0.0 | 29.0 | 19.9 | 14.5 | 27.5 | 20.7 | 27.3 | 17.0 | 26.6 |
| May | 21.8 | 27.4 | 14.4 | 24.5 | 18.7 | 22.3 | 0.3 | 0.0 | 21.7 | 24.3 | 18.2 | 16.7 | 24.4 | 21.6 | 17.9 | 24.6 |
| Jun | 22.0 | 20.4 | 4.5 | 25.0 | 20.7 | 25.3 | 0.4 | 0.0 | 19.2 | 18.9 | 15.2 | 20.6 | 23.0 | 20.5 | 18.9 | 18.2 |
| Jul | 14.3 | 25.7 | 19.9 | 32.8 | 24.2 | 43.3 | 38.3 | 0.0 | 14.5 | 41.7 | 16.8 | 21.3 | 20.6 | 34.1 | 14.2 | 14.2 |
| Aug | 16.6 | 19.8 | 41.7 | 42.8 | 31.1 | 40.0 | 33.3 | 13.8 | 19.5 | 42.1 | 34.4 | 15.1 | 22.9 | 22.6 | 12.1 | 15.9 |
| Sep | 17.1 | 17.7 | 42.3 | 34.8 | 30.6 | 37.0 | 17.7 | 1.0 | 14.7 | 25.8 | 25.9 | 18.4 | 21.9 | 19.5 | 13.5 | 17.6 |
| Percent Time Barrier Closed |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Old River Ag Barrier |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 |
| Oct | 82.0 | 20.9 | 26.2 | 38.7 | 43.7 | 54.3 | 34.2 | 32.6 | 24.6 | 49.8 | 33.6 | 37.6 | 16.5 | 24.0 | 30.7 | 22.0 |
| Nov | 81.6 | 21.4 | 21.7 | 29.7 | 44.2 | 31.4 | 62.3 | 14.8 | 3.6 | 56.3 | 28.9 | 26.2 | 22.3 | 31.8 | 19.9 | 19.3 |
| Dec | 80.2 | 11.9 | 29.1 | 45.4 | 61.0 | 37.2 | 14.4 | 0.0 | 0.0 | 50.5 | 30.2 | 21.2 | 20.7 | 34.0 | 22.3 | 21.5 |
| Jan | 52.2 | 14.0 | 1.1 | 29.7 | 0.6 | 46.1 | 3.4 | 0.0 | 0.0 | 41.6 | 34.7 | 39.4 | 48.2 | 44.1 | 49.2 | 20.0 |
| Feb | 18.8 | 22.5 | 0.0 | 0.5 | 0.0 | 24.7 | 0.6 | 0.0 | 0.0 | 30.5 | 0.0 | 18.4 | 24.7 | 22.6 | 26.9 | 16.7 |
| Mar | 31.9 | 33.7 | 0.0 | 0.8 | 0.0 | 9.7 | 0.0 | 0.0 | 3.9 | 28.1 | 0.0 | 17.9 | 17.0 | 33.0 | 27.3 | 29.0 |
| Apr | 23.9 | 34.9 | 3.3 | 32.0 | 33.7 | 27.8 | 0.0 | 0.0 | 34.0 | 20.5 | 19.5 | 28.6 | 21.3 | 30.1 | 17.4 | 26.9 |
| May | 22.7 | 28.1 | 16.7 | 27.2 | 20.0 | 23.6 | 0.3 | 0.0 | 22.8 | 24.9 | 19.2 | 17.4 | 25.3 | 22.5 | 18.4 | 25.3 |
| Jun | 22.4 | 21.1 | 4.5 | 29.2 | 21.1 | 27.4 | 0.4 | 0.0 | 21.7 | 19.8 | 14.5 | 23.3 | 23.4 | 21.9 | 19.3 | 18.7 |
| Jul | 19.7 | 31.1 | 21.7 | 45.5 | 29.4 | 64.0 | 50.3 | 0.0 | 18.0 | 62.2 | 17.3 | 29.7 | 23.0 | 48.7 | 14.5 | 14.2 |
| Aug | 22.8 | 21.3 | 61.8 | 62.6 | 48.5 | 58.7 | 50.2 | 24.6 | 29.7 | 61.5 | 49.6 | 21.1 | 24.9 | 36.1 | 12.1 | 16.6 |
| Sep | 20.5 | 18.7 | 61.5 | 52.6 | 44.8 | 53.1 | 27.3 | 1.3 | 23.6 | 41.3 | 38.9 | 22.9 | 24.2 | 29.0 | 13.9 | 19.4 |
| Percent Time Barrier Closed |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grant Line Canal Ag Barrier |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 |
| Oct | 72.0 | 14.7 | 18.7 | 29.3 | 33.3 | 39.9 | 26.7 | 21.5 | 18.5 | 38.4 | 26.8 | 29.5 | 12.3 | 18.4 | 22.9 | 16.3 |
| Nov | 72.3 | 15.9 | 16.3 | 22.2 | 33.6 | 24.1 | 51.3 | 10.2 | 1.0 | 44.5 | 22.0 | 19.9 | 16.7 | 25.5 | 14.8 | 14.5 |
| Dec | 64.3 | 7.3 | 20.4 | 33.1 | 44.8 | 25.3 | 9.2 | 0.0 | 0.0 | 35.7 | 20.5 | 15.2 | 14.9 | 27.2 | 16.4 | 16.9 |
| Jan | 35.5 | 10.2 | 0.4 | 15.5 | 0.3 | 30.1 | 1.0 | 0.0 | 0.0 | 29.2 | 24.7 | 26.7 | 33.5 | 32.9 | 37.4 | 15.4 |
| Feb | 12.7 | 16.5 | 0.0 | 0.0 | 0.0 | 14.1 | 0.0 | 0.0 | 0.0 | 19.9 | 0.0 | 11.0 | 17.5 | 17.0 | 20.0 | 12.1 |
| Mar | 25.2 | 26.3 | 0.0 | 0.0 | 0.0 | 6.5 | 0.0 | 0.0 | 1.1 | 20.3 | 0.0 | 12.9 | 12.5 | 23.7 | 21.8 | 20.4 |
| Apr | 17.6 | 27.5 | 1.7 | 23.2 | 24.4 | 20.4 | 0.0 | 0.0 | 26.5 | 15.0 | 15.0 | 21.8 | 15.7 | 22.5 | 12.7 | 21.4 |
| May | 17.7 | 21.1 | 12.4 | 21.4 | 15.5 | 17.4 | 0.0 | 0.0 | 18.1 | 19.5 | 14.4 | 12.9 | 19.7 | 17.1 | 14.0 | 20.3 |
| Jun | 17.8 | 16.4 | 0.0 | 25.7 | 11.7 | 22.8 | 0.0 | 0.0 | 17.2 | 16.1 | 5.4 | 19.7 | 18.8 | 17.8 | 14.7 | 14.7 |
| Jul | 14.7 | 24.6 | 17.5 | 36.4 | 18.8 | 51.8 | 33.9 | 0.0 | 11.8 | 50.3 | 12.8 | 25.2 | 19.2 | 42.4 | 11.0 | 10.6 |
| Aug | 12.3 | 15.1 | 47.4 | 44.0 | 37.0 | 44.1 | 37.0 | 15.4 | 19.7 | 47.8 | 37.5 | 14.8 | 18.5 | 29.7 | 8.1 | 11.6 |
| Sep | 12.6 | 12.7 | 45.2 | 37.1 | 30.4 | 39.6 | 16.4 | 0.6 | 15.8 | 32.1 | 28.4 | 16.4 | 18.0 | 19.3 | 10.5 | 13.5 |

| South Delta Barrier Operations (EIR/EIS Study) |
| --- |
| 2020 Revised Fish Scenario |
| Monthly Breakdown of South Delta Ag Barrier Operations |
| Middle and Old River Full Barrier, Grant Line Canal Special Weir (Crest Level = 1 msl, Oct-May) |
| Percent Time Barrier Closed |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Middle River Ag Barrier |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 |
| Oct | 65.0 | 21.4 | 26.8 | 31.0 | 34.5 | 43.7 | 29.0 | 21.4 | 15.6 | 38.9 | 28.4 | 29.2 | 17.5 | 25.0 | 28.2 | 22.8 |
| Nov | 65.3 | 22.5 | 23.1 | 29.4 | 37.7 | 31.9 | 48.2 | 10.2 | 2.8 | 42.6 | 27.8 | 26.1 | 23.2 | 32.6 | 21.2 | 20.7 |
| Dec | 75.1 | 13.2 | 25.9 | 40.9 | 54.6 | 32.1 | 13.6 | 0.0 | 0.0 | 44.0 | 27.8 | 21.9 | 21.0 | 32.9 | 21.9 | 23.1 |
| Jan | 47.0 | 16.0 | 1.0 | 27.8 | 0.5 | 41.2 | 3.4 | 0.0 | 0.0 | 38.2 | 31.4 | 35.1 | 41.8 | 43.4 | 41.7 | 21.5 |
| Feb | 20.8 | 24.9 | 0.0 | 0.4 | 0.0 | 24.1 | 0.6 | 0.0 | 0.0 | 30.1 | 0.0 | 19.0 | 25.2 | 25.0 | 27.7 | 18.4 |
| Mar | 32.7 | 36.4 | 0.0 | 0.8 | 0.0 | 10.4 | 0.0 | 0.0 | 4.4 | 29.1 | 0.0 | 19.4 | 18.6 | 26.9 | 28.0 | 26.0 |
| Apr | 25.6 | 37.3 | 3.4 | 29.7 | 30.6 | 27.2 | 0.0 | 0.0 | 32.3 | 21.9 | 17.0 | 30.0 | 22.8 | 30.2 | 19.0 | 29.1 |
| May | 24.0 | 30.3 | 15.9 | 26.7 | 20.5 | 24.7 | 0.3 | 0.0 | 24.0 | 26.5 | 20.1 | 18.4 | 27.0 | 23.9 | 20.1 | 27.0 |
| Jun | 23.4 | 22.0 | 4.5 | 27.1 | 21.6 | 27.3 | 0.4 | 0.0 | 20.8 | 20.1 | 15.2 | 22.2 | 24.5 | 22.1 | 20.2 | 19.6 |
| Jul | 15.9 | 27.7 | 21.6 | 37.7 | 26.9 | 51.2 | 44.7 | 0.0 | 15.5 | 49.0 | 18.1 | 23.8 | 21.9 | 38.5 | 15.2 | 15.4 |
| Aug | 18.9 | 21.7 | 48.0 | 51.1 | 35.7 | 46.5 | 38.4 | 15.8 | 22.2 | 49.2 | 39.2 | 17.6 | 25.1 | 26.0 | 13.1 | 17.6 |
| Sep | 19.0 | 19.5 | 48.8 | 40.2 | 35.0 | 42.6 | 20.1 | 1.1 | 17.5 | 30.0 | 29.7 | 20.7 | 24.4 | 22.6 | 15.0 | 19.7 |
| Percent Time Barrier Closed |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Old River Ag Barrier |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 |
| Oct | 89.3 | 23.7 | 28.5 | 43.6 | 49.0 | 62.0 | 39.1 | 33.0 | 25.7 | 56.5 | 38.1 | 42.3 | 18.0 | 26.2 | 36.0 | 24.0 |
| Nov | 87.5 | 24.2 | 23.6 | 35.0 | 51.1 | 34.1 | 69.9 | 15.9 | 3.6 | 63.7 | 33.1 | 28.6 | 24.6 | 36.6 | 21.8 | 21.2 |
| Dec | 80.3 | 13.3 | 30.8 | 46.3 | 61.0 | 37.4 | 15.3 | 0.0 | 0.0 | 50.5 | 31.5 | 24.4 | 23.1 | 37.5 | 25.4 | 23.8 |
| Jan | 52.3 | 16.0 | 1.1 | 29.7 | 0.6 | 46.1 | 3.4 | 0.0 | 0.0 | 41.8 | 34.8 | 39.9 | 48.5 | 48.9 | 49.9 | 21.9 |
| Feb | 22.3 | 25.0 | 0.0 | 0.5 | 0.0 | 25.2 | 0.6 | 0.0 | 0.0 | 32.1 | 0.0 | 20.1 | 27.7 | 25.1 | 29.9 | 18.7 |
| Mar | 38.1 | 36.6 | 0.0 | 0.8 | 0.0 | 10.4 | 0.0 | 0.0 | 4.1 | 31.2 | 0.0 | 21.4 | 19.1 | 33.6 | 31.9 | 29.7 |
| Apr | 26.0 | 37.8 | 4.0 | 35.9 | 38.2 | 31.4 | 0.0 | 0.0 | 37.8 | 22.4 | 20.9 | 31.9 | 23.2 | 34.0 | 19.2 | 29.5 |
| May | 24.8 | 30.7 | 19.6 | 30.6 | 23.1 | 25.9 | 0.3 | 0.0 | 24.8 | 27.4 | 21.6 | 19.2 | 27.7 | 24.7 | 20.3 | 27.5 |
| Jun | 24.8 | 23.1 | 4.5 | 34.4 | 21.7 | 31.3 | 0.4 | 0.0 | 25.8 | 22.6 | 14.8 | 26.9 | 25.4 | 25.1 | 21.4 | 20.6 |
| Jul | 22.8 | 34.8 | 25.9 | 50.8 | 30.3 | 69.9 | 51.0 | 0.0 | 21.0 | 65.9 | 19.1 | 33.8 | 26.2 | 55.4 | 17.5 | 16.3 |
| Aug | 25.0 | 23.3 | 64.5 | 65.7 | 50.4 | 62.9 | 51.5 | 25.3 | 30.7 | 63.9 | 51.1 | 23.9 | 27.0 | 39.7 | 13.7 | 18.6 |
| Sep | 23.4 | 20.8 | 65.5 | 56.7 | 48.2 | 57.5 | 27.9 | 1.3 | 25.2 | 43.8 | 41.4 | 26.8 | 26.4 | 30.9 | 15.7 | 21.4 |
| Percent Time Barrier Closed |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Grant Line Canal Ag Barrier |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 |
| Oct | 87.0 | 22.4 | 26.5 | 41.3 | 45.8 | 56.5 | 37.9 | 26.6 | 22.4 | 53.5 | 37.1 | 40.4 | 17.9 | 26.0 | 33.8 | 23.8 |
| Nov | 85.0 | 24.3 | 23.1 | 32.9 | 48.8 | 32.8 | 68.1 | 13.7 | 1.4 | 61.7 | 31.6 | 27.6 | 24.3 | 35.7 | 21.7 | 21.2 |
| Dec | 73.0 | 10.7 | 25.4 | 40.8 | 54.6 | 31.5 | 12.1 | 0.0 | 0.0 | 44.8 | 25.6 | 19.7 | 19.7 | 33.4 | 21.3 | 22.5 |
| Jan | 42.7 | 14.7 | 0.5 | 19.3 | 0.4 | 37.2 | 1.5 | 0.0 | 0.0 | 36.3 | 29.7 | 32.6 | 40.5 | 41.7 | 44.9 | 20.7 |
| Feb | 17.5 | 22.3 | 0.0 | 0.0 | 0.0 | 19.5 | 0.0 | 0.0 | 0.0 | 25.1 | 0.0 | 15.3 | 22.8 | 22.7 | 26.7 | 16.9 |
| Mar | 32.5 | 35.4 | 0.0 | 0.0 | 0.0 | 8.8 | 0.0 | 0.0 | 1.7 | 25.5 | 0.0 | 17.5 | 17.7 | 28.7 | 28.4 | 24.7 |
| Apr | 25.5 | 38.0 | 2.9 | 33.3 | 36.5 | 29.7 | 0.0 | 0.0 | 37.1 | 21.4 | 18.8 | 30.4 | 22.9 | 33.0 | 19.1 | 29.3 |
| May | 24.9 | 29.9 | 18.8 | 30.2 | 23.2 | 25.1 | 0.0 | 0.0 | 25.2 | 27.6 | 21.8 | 19.2 | 27.5 | 24.9 | 20.8 | 27.9 |
| Jun | 24.6 | 22.8 | 0.0 | 32.5 | 15.9 | 32.0 | 0.0 | 0.0 | 21.9 | 22.5 | 7.6 | 26.8 | 25.5 | 24.8 | 20.8 | 20.6 |
| Jul | 19.6 | 34.7 | 23.3 | 45.9 | 23.5 | 63.4 | 40.1 | 0.0 | 15.6 | 59.1 | 17.6 | 31.2 | 27.0 | 52.3 | 17.3 | 16.3 |
| Aug | 17.1 | 21.6 | 56.9 | 55.7 | 44.9 | 54.3 | 44.3 | 19.6 | 24.8 | 57.2 | 43.3 | 19.5 | 25.6 | 36.6 | 11.9 | 16.8 |
| Sep | 18.2 | 18.8 | 57.6 | 48.8 | 38.7 | 50.8 | 20.6 | 0.7 | 20.6 | 39.5 | 35.2 | 22.0 | 24.3 | 25.4 | 15.1 | 19.4 |

12)	Will operating to 8500 cfs at Harvey O. Banks Pumping Plant (i.e. South Delta Improvement Program) be included in this consultation?  If yes,  include a comparison of current modeling outputs, (i.e. Dave Fullerton’s gaming scenarios, the Natural Heritage Institute EWA model, and the CALSIM II model).  Include use of Joint Point of Diversion (JPOD), the use of an intertie between CVP and SWP, upstream reservoir releases, and a discussion of the Environmental Water Account (EWA) size in relation to impacts on listed salmon or steehead.  Does the proposed long term OCAP assume a long term EWA?

The current assumptions for the OCAP modeling in light of the recent SDIP-Project Integration agreement made in Napa between SWP and CVP for the Future CALSIM II modeling are:

- Freeport RWP. EBMUD diversion to be treated as an exporter in regard to COA obligations.

- SDIP. Banks PP to be simulated at a permitted capacity of 8500 cfs in all months. Assumptions and code consistent with DWR SDIP “Exporter” version.  500 cfs assumed to be reserved for EWA July-September.

- DMC/CA Intertie. Intertie to be simulated with capacity of 400 cfs. Assumptions and code consistent with USBR Intertie “Full Use” study provided by Nancy Parker.

- 100,000  acre-feet Conveyance (II.1).  SWP to convey 100,000 af of Level 2 refuge water each year at Banks PP.  For modeling purposes, conveyance assumed to occur in July and August with 50,000 af in each month.  CVP supplies, as defined by COA, will be conveyed for this purpose prior to be being labeled “abandoned” supplies.  Conveyance will only occur after Tracy capacity is maximized.

- NOD Accounting Adjustments (II.2).  CVP will provide the SWP with up to 75,000 af of water to meet in-basin requirements through adjustments in COA accounting of responsibilities. For modeling purposes, the provision of water will be simulated as a transfer of CVP storage in Shasta to the SWP beginning in March of each year and updated in April and May. The actual amount transferred to the SWP will be determined by multiplying the CVP SOD Ag allocation percentage by the 1,000 af, up to a maximum of 75,000 af.

An SWP account will be simulated in Shasta and treated in the same manner as SWP water in Oroville. COA accounting will be adjusted to reflect releases from this account as SWP share of in-basin obligations. SWP will attempt to release this water prior to Oroville supplies since no year-to-year carryover will be permitted. SWP water in Shasta will be considered “unspillable” for the current year.

- Simulation Procedure.   The simulation will initially consist of a four step study, D1485-D1641-B2-SDIP-Integration.

- B2 Accounting.  The SDIP and Integration provisions are desired to be considered as post-B2 for accounting purposes. CVO has recommended that the Intertie be included in the accounting of the B2 baseline.  The code sets for SDIP, Intertie, and Integration will be included in all steps of the simulation, but only the Intertie will be activated pre-B2. SDIP and Integration will be implemented post-B2 so as to not effect B2 accounting.

- North Bay Aqueduct:  Two-thirds of the NBA will be treated as an exporter.

- EWA: Is to be included in the OCAP consultation as a Today case and Future Case.  EWA will be modeled by taking actions at the CVP and SWP delta export facilities (Tracy and Banks pumping plants).  Table X below shows what actions are taken by either the 40-30-30 Index or 60-20-20 Index and which facility the actions can occur on.  The debt and assets of these actions will be tracked and accounted for as well as debt spilling.

Table X. EWA Actions Amounts or occurrences by 40-30-30 Index for Dec – Mar and 60-20-20 for VAMP Shoulders, VAMP and June Ramping

| 40-30-30 | Dec | Jan | Feb | Mar |  | Apr Shld | VAMP | May Shld | Jun |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Banks/Tracy/Both | Both | Both | Both | Both | 60-20-20 | Both | Banks | Both | Both |
| Wet |  | 50 | 50 |  | Wet |  | On | On | On |
| AN |  | 50 | 50 |  | AN |  | On | On | On |
| BN |  | 50 | 50 |  | BN |  | On | On | On |
| D |  | 50 | 50 |  | D | On | On | On | On |
| C |  | 50 | 50 |  | C | On | On | On | On |

Modeling output of the current and future CALSIM II simulations are in Chapter 8 of the BA and Appendix X of the OCAP BA.

13)	Discuss how the results of the Vernalis Adaptive Management Plan (VAMP) studies are expected to affect the proposed long term OCAP and San Joaquin River steelhead populations?

The following two paragraphs describe how the VAMP fits into the CVP as described in the OCAP document.  Currently VAMP is in the 3rd year of a 12-year experiment.

Adopted by the SWRCB in D-1641, the San Joaquin River Agreement (SJRA) includes a 12-year experimental program providing for flows and exports in the lower San Joaquin River during a 31-day pulse flow period during April-May. It also provides for the collection of experimental data during that time to further the understanding of the effects of flows, exports, and the barrier at the head of Old River on salmon survival. This experimental program is commonly referred to as the Vernalis Adaptive Management Program (VAMP). Within the SJRA, the IPO has been assumed as the baseline operation for New Melones Reservoir which forms part of the existing flow condition from which flows will be provided on the San Joaquin River to meet the target flows for the 31-day pulse during April-May. Additional flows needed to meet the targets will be provided from other sources in the San Joaquin River under the control of the parties to the SJRA.

CVP-SWP operations forecasts include Vernalis flows that meet the appropriate pulse flow targets for the predicted hydrologic conditions. The flows in the San Joaquin River upstream of the Stanislaus River are forecasted for the assumed hydrologic conditions. The upstream of the Stanislaus River flows are then adjusted so that when combined with the forecasted Stanislaus River flow based on the IPO, the combined flow would provide the appropriate Vernalis flows consistent with the pulse flow target identified in the SJRA. An analysis of how the flows are produced upstream of the Stanislaus River is included in the SJRA EIS/EIR. For purposes of CVP-SWP operations forecasts, the flows are simply assumed to exist at the confluence of the Stanislaus and San Joaquin rivers, and the assessment of CVP-SWP operations in the Delta effects begins downstream of that point.

No evaluation of the effects of the VAMP flows on steelhead has been done.  The VAMP flows are timed to coincide with the end of the peak salmon movement through the Delta each year.  VAMP studies have shown that the pulse flows provide outmigration benefits to the hatchery released juvenile Chinook salmon used for the VAMP study and to naturally spawned Chinook salmon.  Peaks in juvenile Chinook outmigration in the tributaries (eg Stanislaus) tend to occur during the flow changes, ie. when flows are increasing and again when they are decreasing.  Chinook outmigration occurs at a higher rate during the sustained pulse flows than during lower flows.  Steelhead benefits are harder to quantify.  Their larger size makes them harder to monitor because they can more easily avoid common sampling gear.  In addition there are much fewer steelhead than salmon around to monitor.  Steelhead are believed to respond similarly to pulse flows and those that are ready to outmigrate when the pulse flows occur probably do outmigrate and benefit from the VAMP flows and barrier operations.    During 2001 VAMP sampling, two steelhead were captured at the head of Old River barrier culverts.  One steelhead was captured there in 2002.  Steelhead were also captured at Antioch (28 in 2001 and 102 in 2002) and Chipps Island (28 in 2001 and 30 in 2002) during VAMP sampling.  This indicates that at least some juvenile steelhead are in the system during VAMP and potentially benefit.  VAMP flows should conceptually provide survival benefits to San Joaquin River juvenile steelhead and result in more returning adults.  Actual benefits and population effects may not be quantifiable in the near future.

14)	Describe how CVP/SWP operations will change with respect to the recent CVPIA 3406(b)(2) court rulings and the Department of the Interior (DOI) draft decision.  The BA should include a thorough discussion of the anticipated effects of the decision on listed salmon and steelhead both upstream and in the Delta.

Table X shows a summary of the 3406(b)(2) May 9th, 2003 decision by the Dept. of the Interior.  The fall target of 200,000 acre-ft should benefit listed salmon and steelhead.  The operation/implementation of 3406(b)(2) will be done through the B2IT, the EWA Team, and the WOMT to coordinate the (b)(2) fishery action plan.

Table X. Summary of the May 9, 2003 3406(b)(2) Decision

| Area | 2003 Revised Decision |
| --- | --- |
| Introduction | Incorporates parts of the October 5, 1999, Final Decision upheld by the District Court, modifies other parts and adds new components. |
| Calculation of Yield | 5,990,000 acre-feet |
| Process and Accounting Accounting Period Accounting Methodology | A. October 1 to September 30 B. Two accounting metrics; a release metric and export metric. Eliminate reset and offset. Add export limitation of 640,000 acre-feet. Fall target is 200,000 acre-feet. |
| Modifications to CVP Operations | Paragraph to describe 3406(b)(1), reoperation. Replaced some language with text from the CVPIA section 3406(b)(1). |
| Water Banking and Transfer/Exchanges of Water | Interior will develop a banking/ transfer policy. |
| Water to meet Water Quality Control Plan (WQCP) Obligations | Now called Water to Meet WQCP/ESA Obligations. Eliminated the 450,000 acre-feet cap on WQCP. |
| Shortage Criteria | Based on 40-30-30 (Sac Valley) Index Year Type, during Critical and Dry years and allocation of Northern Agricultural Water Service Contracts. . |
| Coordination | Added coordination with Water Operations Management Team (WOMT) and Environmental Water Account (EWA) Team. |

15) 	Describe how Reclamation intends to operate the CVP after the proposed Freeport Diversion is completed as scheduled in 2007.  Which reservoirs will be used to make releases for this new diversion?  What will be the effect on listed salmonids of Dry or Critical Year upstream releases to meet the EBMUD allocation?  Include water temperature effects on winter-run Chinook salmon survival using the Sacramento River Salmon Model (refer to CVP-OCAP dated October 1992, pg 125).

The Freeport Diversion will be operated as stated in the Biological Assessment for the Freeport Regional Water Authority (USBR and Freeport Regional Water Authority, December 2002).  For modeling results on the Incremental Analysis of the Freeport Project please see the modeling results from the Biological Assessment for the Freeport Regional Water Authority.  From the BA the operations and sources for the diversion are as follows:

Sacramento County Water Agency

Water Supply

SCWA’s primary potential sources of water for Zone 40 are the P.L. 101-514 CVP water supply contract, commonly known as the Fazio contract, an assignment of a portion of Sacramento Municipal Utility District’s (SMUD’s) existing CVP water supply contract, appropriative water rights on the American and Sacramento Rivers, and groundwater in the central county basin.  Table 1 summarizes the total anticipated surface water supplies from these sources assumed for facility planning.  Each of these sources is described below, following a brief summary of the Sacramento Area Water Forum Agreement, which sets the stage for some of the information presented later.

Table 1.  Total SCWA Existing and Anticipated Surface Water Supplies1

| Surface Water Entitlement | Entitlement Amount (acre-feet per year [af/yr]) | Estimated Long-Term Average Use2 |
| --- | --- | --- |
| CVP water supply contracts | 15,000 | 12,0003 |
| SMUD CVP contract assignments | 30,000 | 25,000 |
| Appropriated water | Undetermined | 20,000 |
| Other water supplies | Undetermined | 10,000 |
| Total long-term average use |  | 67,000 |
| 1 Long-term average use of each individual supply is subject to minor change resulting from refinement of CALSIM modeling runs for FRWP EIS/EIR. Total long-term average use will remain fixed at 67,000 af/yr. 2 Based on 73-year historical hydrology. 3 8,000 af/yr to be diverted at SRWTP. |

Sacramento Area Water Forum Agreement

Public agencies in the Sacramento area are involved in a cooperative effort, known as the Sacramento Area Water Forum (Water Forum), designed to explore acceptable project alternatives that could bring additional high-quality water to Sacramento County, the City of Sacramento, and entities in Placer and El Dorado Counties.  The common goal is to provide a safe, reliable water supply for the entire region while preserving fishery, wildlife, recreational, and aesthetic values along the lower American River.

The Water Forum is a diverse group of business and agricultural leaders, citizen groups, environmentalists, water managers, and local governments in the Sacramento area.  In 1995, these groups were joined by water managers in Placer and El Dorado Counties (Sacramento Area Water Forum 1999).  The members of the Water Forum developed a Water Forum Proposal for the effective long-term management of the region’s water resources.  The Water Forum Proposal was analyzed and reviewed in an EIR prepared and certified by the City and County of Sacramento. To signify approval of the Proposal, 40 Water Forum members signed the Water Forum Agreement in April 2000.

To achieve the Water Forum goals, all signatories of the Water Forum Agreement need to support and, where appropriate, participate in seven elements of the agreement.  These elements are

increased surface water diversions,

actions to meet customers’ needs while reducing diversion effects on the lower American River in drier years,

support for an improved pattern of fishery flow releases from Folsom reservoir,

lower American River habitat management,

water conservation,

groundwater management, and

participation in Water Forum successor effort.

SCWA participated in the Water Forum process and is a signatory to the Water Forum Agreement.  The Water Forum Agreement supports SCWA’s pursuit of additional water supplies and includes SCWA’s need for increased surface water diversions.  SCWA’s “Purveyor Specific Agreement” also commits it to certain limitations on its use of water supplies.  SCWA agreed to divert surface water at or near the mouth of the American River or from the Sacramento River.  It agreed to limit its surface water diversions to 78,000 af and to meet strict water conservation requirements specified in the Water Forum Agreement that are to be applied throughout the Sacramento region.  In addition, the Water Forum Agreement sets the sustainable yield of the central county groundwater basin, from which SCWA pumps, at 273,000 af/yr.  Of that yield, SCWA expects to be able to produce a long-term average of approximately 41,000 af/yr.

Central Valley Project Water Supply Contracts

In 1999, SCWA contracted with Reclamation for a CVP water supply under Public Law 101-514.  This contract provides for the delivery of up to 22,000 af/yr to meet the needs of Sacramento County, with up to 7,000 af/yr of this amount delivered to the City of Folsom through a subcontract.  Under this contract, SCWA is authorized to receive up to 15,000 af/yr depending on actual water needs and provided that it fully uses existing water entitlements within Sacramento County, implements water conservation and metering programs within the contract service area, and implements programs to maximize the conjunctive use of surface water and groundwater.  This contract provides for Reclamation to reduce deliveries by up to 25% from the contract maximum during years when low runoff limits CVP supplies.

Sacramento Municipal Utility District Central Valley Project Contract Assignments

The Sacramento Area Water Forum supports the development of water transfers and water contracts with existing entitlement holders.  Consistent with the Water Forum Agreement, an agreement-in-principle has been signed between Sacramento Municipal Utility District (SMUD), the City of Sacramento, and SCWA.  SMUD has an existing Reclamation contract.  Under a separate agreement implementing the agreement-in-principle, two assignments totaling 30,000 af/yr of water would be made to SCWA, to be treated and conveyed through the City’s facilities for delivery to Zone 40.  As part of the Water Forum Agreement, SCWA’s Zone 40 would provide groundwater supply and delivery facilities to meet SMUD’s dry-year water shortages.

The agreement to effectuate both assignments is currently being negotiated.  The potential environmental effects of both assignments are undergoing CEQA environmental review and are being addressed further under the EIR/EIS for the proposed FRWP.

Appropriative Water Rights

On May 30, 1995, the Sacramento County Board of Supervisors approved the submittal of an application to the State Water Resources Control Board (SWRCB) for the appropriation of water from the American and Sacramento Rivers.  The amount of water acquired will be determined after a hearing before the SWRCB.  The water, estimated to be diverted at an average rate of 20,000 af/yr, could be used in conjunction with existing groundwater supplies to increase long-term groundwater yields.  The potential environmental effects of using this supply are being assessed in the EIR/EIS for the FRWP.

Other Water Supplies

As Zone 40 approaches buildout conditions in the future, more reliance on other sources of water or methods of supplementing groundwater yields will be necessary to comply with long-term average operational groundwater yield limitations while meeting buildout demand.  Possible options for meeting this demand could involve the following actions:

supplementing natural recharge during wet years with existing supplies,

acquiring water through transfers from other water users upstream of SCWA diversion points,

using the City of Sacramento’s American River entitlements in that area of Zone 40 that is within the City’s authorized American River Place of Use,

using reclaimed water from the Sacramento Regional Wastewater Treatment Plant (Regional Plant) on an exchange basis, or acquiring additional appropriated water.

East Bay Municipal Utility District

Water supply forecasts are used in the preparation of operation projections.  The water supply forecast is a March 1 forecast of EBMUD’s October 1 total system storage, as revised monthly through May 1 as more reliable information becomes available.  The main parameters considered in the operation projection are the water supply forecast of projected runoff, water demand of other users on the river, water demand of EBMUD customers, and flood control requirements.  Under these conditions, EBMUD would take delivery of Sacramento River water through the new intake facility to supplement its water supplies and retain storage in its Mokelumne River and terminal reservoir systems.

EBMUD plans to take Sacramento River water in an EBMUD dry year, under the terms of its Amendatory Contract with Reclamation.  An EBMUD dry year is defined as any year in which EBMUD’s March 1 forecast of its October 1 total system storage is less than 500,000 af based on a 50% exceedance, or any different reasonable exceedance used by EBMUD to declare rationing within the service area, or as otherwise agreed to by EBMUD and Reclamation.  During an EBMUD dry year, EBMUD is entitled to take delivery of up to a total of 133,000 af of CVP water (subject to 25% cutback in allocation; total available is 112,000 af/yr) in any one year in which EBMUD’s total system storage forecast remains below 500,000 af, not to exceed 165,000 af in any consecutive 3-year drought period.  EBMUD plans to take Sacramento River water at a maximum diversion rate of 100 million gallons per day (MGD) during an EBMUD dry year as defined above.  Diversions would cease when EBMUD end-of-March projections indicate that total system storage is expected to remain above 500,000 af at the end of September, as EBMUD has no requirement for Sacramento River water during EBMUD wet years.  The delivery limitations mandated in the Hodge Decision would not apply to this delivery location, as the delivery of water would not occur on the lower American River.

During a planned outage of EBMUD’s Mokelumne River facilities, such as for major maintenance or seismic improvements, EBMUD would take delivery of up to 155 cfs of water from the new intake for direct use by its customers.  Planned outages would occur infrequently and total no more than 12 months in a 20-year period, with no single event extending beyond 6 months.

16)	Provide an estimate of the daily loss rate for juvenile steelhead at the TFCF, Skinner (SWP) Fish Facility and Rock Slough Intake, which would include predation rates (i.e., pre-screen loss), louver efficiencies, and trucking/handling loss, so that incidental take levels can be determined.  This estimate was specified in Term and Condition 6(b) of the interim OCAP biological opinions dated May 8, 2001 and September 20, 2002 .

# TFCF (CVP) and Skinner (SWP)

The Delta serves as a migration corridor to the upper Sacramento and San Joaquin river basins for adult and juvenile steelhead. It may also serve as a rearing habitat for juveniles that move into the Delta before they enter salt water, but this has not been studied. Presumably, one of the anthropogenic factors that may influence steelhead abundance and distribution in the Delta is CVP and SWP operations. However, little data are available to determine the extent to which CVP and SWP Delta operations affect steelhead population abundance. However, we present what little data are available as an initial assessment of potential effects.

DWR and USBR (1999) reported significant linear relationships exist between total monthly export (January through May) and monthly steelhead salvage at both Delta fish facilities. The months included in the analysis were based on months that steelhead consistently appeared in salvage between 1992 and 1998. Scatterplots of 1992 through 2000 CVP and SWP steelhead salvage versus exports are shown in Figure 0–1 and Error! Reference source not found., repectively. A generalized linear modeling approach confirmed that salvage and total monthly exports are positively correlated, at least at the SWP (Michael Chotkowski, personal communication, 2000).

Figure 0–1 Scatterplot of total monthly CVP export in acre-feet versus log10 total monthly CVP steelhead salvage, 1992–2000.

January data (filled), February through May data (open), June data (gray).

Figure 0–2 Scatterplot of total monthly SWP export in acre-feet versus log10 total monthly SWP steelhead salvage, 1992–2000.

January data (filled), February through May data (open).

At least two factors confound interpretation of these results, making future take predictions based on past salvage very dubious (Figure 0–3; Michael Chotkowski, personal communication, 2000). First, there has been a decrease in steelhead salvage since 1992 (Figure 0–4). This is presumably due to changes in the timing of exports from spring to summer resulting from implementation of the Bay-Delta Accord. An alternative hypothesis is that steelhead abundance has continually declined, but this seems less likely since the returns to Nimbus and Feather River hatcheries since 1992 (Figures 2-6 and 2-7). Interestingly, returns to these hatcheries are not correlated to each other (Spearman R = –0.32, P = 0.09). The lack of correlation in returns to Nimbus and Feather River hatcheries does not support the hypothesis that a single factor like Delta operations has a dominant effect on the abundance patterns of all Central Valley steelhead.

Figure 0–3  Predicted steelhead salvage at the SWP Delta fish facilities in relationship to exports (95% confidence intervals) based on a generalized linear model of historical salvage and export data for the January through May period, 1992–1999

In addition to being correlated to amount of water exported, steelhead salvage is also positively correlated to December through June CPUE of steelhead in the USFWS Chipps Island Trawl (Spearman R = 0.89, P = 0.02; Figure 0–4), which we consider the best available estimate of juvenile steelhead year class strength. In other words, the Delta facilities take more steelhead when there are more steelhead. This suggests steelhead salvage at the facilities is an indicator of juvenile year class strength. A similar relationship has been found for splittail (Sommer and others 1997). Both the steelhead and splittail relationships with salvage contrast those reported for delta smelt and longfin smelt, species whose abundance estimates are somewhat inversely correlated to salvage. In other words, the effects of entrainment are greatest in the years when smelt abundances are lowest. Like the hatchery data presented above, the Chipps Island data, which includes both hatchery and naturally spawned juveniles, do not indicate steelhead numbers have continually declined since year-round sampling was initiated in 1994.

The currently available data suggest salvage represents small percentages of hatchery and wild steelhead smolts.  The estimated percentages of hatchery smolts in combined (SWP and CVP) salvage ranged from 0.01% to 0.4% of the number released from 1998 through 2000.  The estimated percentages of the wild steelhead smolt populations salvaged were higher, but were still less than 1% each year and ranged from 0.06% to 0.9% (Nobriga and Cadrett 2001). A high percentage of the unclipped steelhead captured at the CVP salvage facility in 2003 had fin erosion indicating they were likely hatchery fish.  These fish are currently counted as unclipped and assumed to be wild.  Lloyd Hess (personal communication 2003) recommended updating the data sheet to include unclipped steelhead that display physical characteristics of hatchery reared steelhead. Table 0–2 shows total salvage of unclipped steelhead from 1993 through March 2003 and Table 0–3 shows average salvage of steelhead from 1981 through 2002.

Table 0–1  Combined marked and unmarked steelhead salvage for the 1994 through 2002 emigration seasons (for example, 1994 = October 1993 through July 1994), and percentage of combined salvage occurring between the December through June period depicted in Figure 3-3.

| Emigration season | Combined salvage | Percent of salvage from December through June |
| --- | --- | --- |
| 1992 | 18,729 | 100 |
| 1993 | 18,583 | 100 |
| 1994 | 1,594 | 100 |
| 1995 | 2,605 | 100 |
| 1996 | 5,376 | 100 |
| 1997 | 1,057 | 88 |
| 1998 | 926 | 82 |
| 1999 | 2,544 | 99.5 |
| 2000 | 9,463 | 96 |
| 2001 | 12,909 | 99 |
| 2002 | 3,590 | 100 |

Figure 0–4  Relationship between total combined CVP and SWP steelhead salvage December through June, and December through June steelhead catch per minute trawled at Chipps Island, December 1993 through June 1999

Table 0–2  Salvage of unclipped steelhead, 1993 – March 2003 at the CVP and SWP delta fish salvage facilities.

| Year | CVP | SWP | Total |
| --- | --- | --- | --- |
| 1993 | 6,864 | 9,673 | 16,537 |
| 1994 | 974 | 337 | 1,311 |
| 1995 | 1,176 | 993 | 2,169 |
| 1996 | 1,966 | 3,117 | 5,083 |
| 1997 | 564 | 205 | 769 |
| 1998 | 420 | 41 | 461 |
| 1999 | 1,426 | 942 | 2,368 |
| 2000 | 1,666 | 2,257 | 3,923 |
| 2001 | 1,637 | 2,834 | 4,471 |
| 2002 | 959 | 686 | 1,645 |
| 2003 | 737 | 1,015 | 1,752 |
| Total 1993 – March 2003 | 18,389 | 22,099 | 40,488 |

Table 0–3  Average monthly total (clipped and unclipped) steelhead salvage at the delta fish facilities, 1981 – 2002.

|  | SWP | CVP | Total |
| --- | --- | --- | --- |
| January | 438 | 475 | 913 |
| February | 1,465 | 917 | 2,382 |
| March | 1,687 | 1,223 | 2,910 |
| April | 1,488 | 573 | 2,060 |
| May | 302 | 270 | 572 |
| June | 56 | 27 | 84 |
| July | 14 | 75 | 89 |
| August | 4 | 0 | 4 |
| September | 0 | 0 | 0 |
| October | 24 | 0 | 24 |
| November | 149 | 16 | 165 |
| December | 171 | 259 | 430 |

Our assessment may be confounded by hatchery fish, which constitute the majority of steelhead in the Central Valley (Error! Reference source not found.). Since 1998, Central Valley hatcheries have attempted to clip the adipose fins of all hatchery-produced steelhead, enabling us to estimate the proportion of naturally spawned steelhead smolts emigrating through the Delta. The proportions of adipose fin-clipped steelhead are shown in

Table 0–4.

Table 0–4  Percentage of steelhead salvage at the CVP and SWP fish facilities with adipose fin clips, 1993 – March 2003.

| Year | CVP | SWP | combined |
| --- | --- | --- | --- |
| 1993 | 1 | 4 | 3 |
| 1994 | 3 | 7 | 4 |
| 1995 | 1 | 3 | 2 |
| 1996 | 8 | 2 | 4 |
| 1997 | 2 | 11 | 5 |
| 1998 | 44 | 47 | 45 |
| 1999 | 5 | 11 | 7 |
| 2000 | 44 | 65 | 58 |
| 2001 | 64 | 65 | 65 |
| 2002 | 42 | 68 | 56 |
| To Mar. 2003 | 89 | 81 | 85 |

If hatcheries continue to clip the adipose fins of all hatchery-reared steelhead, the USFWS Chipps Island trawl may eventually also be a useful tool for devising an emigration abundance index specifically for naturally-spawned steelhead that can be compared to salvage or other potential influencing factors.

# CCWD’s Intakes

## Rock Slough Old River Intake

The Rock Slough diversion diverts water from Old River into the Contra Costa Canal. The historical diversion pattern varied between 50 to 300 cfs (Jerry Morinaka 1998, 2003 pers. comm., Table 0–2), with the higher pumping rates typical of the late spring through late fall period. The diversion is presently unscreened and construction of a fish screen is directed under CVPIA and included in the District’s biological opinion for the Los Vaqueros project.  The USBR in collaboration with CCWD is responsible for constructing the fish screen.  Reclamation has requested an extension to the December 2003 deadline to complete the Rock Slough fish screen.  Reclamation is asking for an extension until December 2008 to allow completion of current CALFED project studies that might affect frequency of usage of the Rock Slough intake and therefore the screen design.

The extrapolated numbers of steelhead entrained by the facility between 1994 and 1996 were low, ranging from 52 to 96 per year (Morinaka 1998). Additional losses (8% to 30%) were recorded from the remains of fish killed during passage through the intake. Further losses could have occurred through predation due to the facility’s location at the end of a dead-end slough, but this was not assessed for steelhead.

The following is a summary of fisheries monitoring conducted at Rock Slough since 1994.  Numbers of listed fish species captured during monitoring is shown in Table 0–1.

### Fish Monitoring Program at Pumping Plant #1

#### 1994 to beginning of 1997

- Sample with a sieve-net in the Contra Costa Canal

- Sampled approximately 90 – 100% of the flow of water

- Sampled for an 8-hour period each sampling effort

- Year round monitoring program:

February through May = every other day

June and July = every 4th day

August and September = once a week

October through January = every 4th day

- Rock Slough was the primary source to meet the water demands in the Contra Costa Canal throughout this monitoring program

### Fish Monitoring Program at the Headworks Location (Rock Slough Intake)

#### 1998 to present

- Sampled with a sieve-net at the headworks structure of the Contra Costa Canal intake channel (4 miles upstream of Pumping Plant #1)

- Sampled approximately 10 – 15% of the flow of water

- Sampled for periods of 3 to 5 hours

- Year round monitoring program (once a week throughout the year)

- Rock Slough intake was used less after 1998 when Los Vaqueros Reservoir and the Old River Pumping Plant were operating

Table 0–1  Numbers of listed fish species captured at Pumping Plant # 1 of the Contra Costa Canal and the headworks at the Rock Slough Intake during fisheries monitoring, 1994 – 2002

|  | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Chinook Salmon (All Races) | 101 | 95 | 40 | 0 | 1 | 0 | 3 | 0 | 0 |
| Winter-Run Sized Chinook Salmon | 2 | 6 | 4 | 0 | 1 | 0 | 0 | 0 | 0 |
| Spring-Run Sized Chinook Salmon | 29 | 54 | 25 | 0 | 0 | 0 | 0 | 0 | 0 |
| Steelhead | 10 | 14 | 12 | 0 | 0 | 0 | 0 | 0 | 0 |
| Delta Smelt | 2 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 |
| Splittail | 1 | 1057 | 8 | 0 | 0 | 1 | 0 | 0 | 0 |

Table 0–2  Average monthly diversion rate at the Rock Slough intake, 1998 – 2002

| Contract | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Year | cfs | cfs | cfs | cfs | cfs | cfs | cfs | cfs | cfs | cfs | cfs | cfs |
| 1998 | 35 | 28 | 38 | 69 | 102 | 115 | 132 | 159 | 171 | 139 | 107 | 88 |
| 1999 | 40 | 38 | 28 | 64 | 8 | 147 | 218 | 140 | 18 | 3 | 2 | 21 |
| 2000 | 8 | 15 | 28 | 73 | 20 | 149 | 100 | 149 | 155 | 54 | 35 | 13 |
| 2001 | 40 | 37 | 31 | 68 | 48 | 166 | 29 | 32 | 9 | 10 | 13 | 13 |
| 2002 | 6 | 6 | 38 | 60 | 31 | 165 | 146 | 22 | 18 | 10 | 11 | 17 |

The extrapolated numbers of juvenile Chinook salmon (all races) entrained by the facility between 1994 and 1996 ranged from 262 to 642 per year (Morinaka 1998). Additional losses due to predation and fish being killed passing through the intake were estimated using juvenile marked hatchery fall-run Chinook salmon in 28 release groups. Survival estimates (estimated from recaptures in a sieve net 60 feet downstream of Pumping Plant #1) ranged from 0% to 51% and averaged about 18%. The large variation in survival rates may have resulted from releases done at different times of day and with different numbers of fish (see Morinaka 1998 for details). If we assume that only about 20% of salmon passing through the pumping plant survive, then the estimated numbers of juvenile salmon (all races) entrained between 1994 and 1996 would be about 1,695, 3,210 and 1,310 respectively.

Because most diversions occur during the summer months when salmon and steelhead are not present in the vicinity of the diversion and very few listed fish species (1 winter run and 1 splittail) have been captured during monitoring since 1997, the Rock Slough diversion is not believed to be a significant source of mortality for any of the listed species.

17)	Provide CALSIM II modeling which includes the newly emerging pattern of increased releases from Shasta Reservoir as observed over the last three years, due to the Rice Decomposition Program during the fall months. This new demand for water in the upper Sacramento River Basin is not included in current CVP forecasts. Effects of CVP operations in support of this new program need to be addressed in the BA (specifically effects on water temperature in the upper Sacramento River and salmon spawning redd dewatering resulting from instream flow reductions not currently considered in operational forecasts).

The 2001 and 2020 Level of Development hydrologies that are being used for the OCAP models do not incorporate the Rice Decomposition Program but future CALSIM hydrologies will.  The following text is from a study that DWR provided CVO is a research paper that describes the amounts and timing of water use in future CALSIM hydrologies.

Rice Straw Decomposition

And Water Use

Rice straw management in California’s Central Valley has undergone profound changes over the past decade.  Historically, rice growers routinely burned their field to dispose of rice straw for sanitation and seedbed preparation processes.  In 1989, when 400,000 acres of rice were grown in California, 95% of the resulting debris was burned in the field, creating air pollution in the Central Valley and statewide. (Bird, et. all)  The Connelly-Areias-Chandler Rice Straw Burning Reduction Act of 1991 (Phase Down Act) mandated the phase down of rice straw burning in California’s Sacramento Valley.  The practice of burning away rice stubble is now limited to disease-control burning and may not exceed 25% of total rice acreage for the year or 125,000 acres, which ever is less  (California Air Resources Board).   The following Table contains the “Phase Down” beginning in 1992:

| Year | Maximum Acres Allowed to be Burned | Actual Acres Burned |
| --- | --- | --- |
| 1992 | 90% | 303,000 |
| 1993 | 80% | 307,000 |
| 1994 | 70% | 295,000 |
| 1995 | 60% | 260,000 |
| 1996 | 50% | 210,000 |
| 1997 | 38% | 140,000 |
| 1998 | 25% (modified to 200k) | 137,000 |
| 1999 | 25% (modified to 200k) | 139,000 |
| 2000 | <25% or 125,000 | 135,000 |
| 2001 | <25% or 125,000 | <125,000 |
| 2010 | <25% or 125,000 | <100,000 |

The phase down of rice straw burning has required growers to gradually shift to alternative straw management practices.  Non-burn alternatives include soil incorporation of the straw and off-field utilization.  Few commercial viable markets for rice straw exist so most rice straw is soil incorporated.

Rice straw that is incorporated into the soil is decomposed by microorganisms, including bacteria, fungi, and actinomycetes.  Incorporation of the straw increases the number of these decomposers over time.  Microorganisms need oxygen, nutrients (from soil and crop residues), moisture, and heat to become active decomposers.  In dry soil, there is not enough water present to support microbial activity.  To ensure that the straw decomposition process is not limited by moisture, growers are now using supplemental winter irrigations techniques to jumpstart the microbial process in the critical fall period just after harvest.

Principles of Straw Management

A typical on-farm rice decomposition process involves:

(Chop and Spread Straw

Chopping straw and spreading it evenly to improve decomposition rates and reduce clumping of straw matter.

(Incorporate in Fall

Take advantage of warmer weather by incorporating straw into the soil as soon as possible after harvest with a stubble disk, roller, or plow.

(Provide Adequate Moisture

Ensure adequate moisture with irrigation, flooding, or trapping winter water.  Moisture is particularly important during warmer months just after harvest.

# Water Use for Rice Decomposition

Approximately 75% of rice fields are no longer allowed to burn rice straw and now must use new practices to decompose crop residue.  Many farmers have begun to use a winter flood incorporation system to deal with the rice straw, while farms where water is not available and funding is limited must rely on a non-flood incorporation system.  Incorporation methods used depends on several factors including type of equipment available, interest in providing waterfowl habitat, water availability, and cost.  Decomposition can be categorized as Flood and Non-flood incorporation systems.

## Non-Flood Incorporation Systems

Non-flood incorporation systems rely on field preparation, which is described in the following bullets:

- Soon after harvest, incorporate straw thoroughly using a stubble disc or other suitable equipment.  Stubble discs with large blades (32 inches or more), wide spacing and ample frame clearance help prevent piling of the straw.

- Although this method does not rely on flooding, moisture is essential to aid in the decomposition of rice straw.  If rainfall is low, supplemental irrigation may be needed to promote decomposition.

- In the spring, fields may benefit from a light disking prior to deeper tillage.  This disking can help dry soil, promote further decomposition, and prepare the soil for seeding.  Land planning has a new role because it grinds the remaining straw into finer pieces improving incorporation in the final seedbed.  (Brandon, et all)

## Winter Flood Incorporation Systems

Flood operations are described as follows:

- Flood fields as soon after harvest as possible.  Early flooding allows more time for decomposition and encourages waterfowl activity.  The initial flood should be 2-4 inches deep.  This depth should reduce straw movement and clumping caused by wave and wake action produced during rolling.

- Roll straw into mud about one week after flooding.  The soil should be soft enough for straw to be mashed into it, but still firm enough to support equipment.  Rollers with greater weight and penetrating surfaces improve straw/soil contact.

- Straw may also be incorporated into the soil with a stubble disc or other implement prior to flooding.  This practice appears to improve decomposition rates compared to flooding, but buries waterfowl feed.  Shallow rototilling prior to flooding can achieve adequate soil contact comparable to wet rolling.

- After straw is incorporated into mud, the depth of the flood may be increased to 4 to 6 inches, if water is available.  Set field outlets and boxes to capture rainfall and keep field flooded during fall and winter.  Drain fields by late February or early March to allow adequate soil drying.  The straw mat that forms in some winter flooded and rolled fields slows drying and can delay spring tillage operations.  (Brandon, et all)

Farmers have expressed a higher degree of satisfaction in winter flood incorporation opposed to a system that uses only rainfall and/or irrigation but does not remain flooded throughout the winter. (Williams)  Water levels of flooded fields usually remain at 4-6 inches throughout the winter season, although this number varies and is often higher in fields that are used for wildlife conservation and recreation (duck hunting).  Rice farmers interviewed indicate that winter water use for rice straw decomposition is between 1 and 2.5 AF/acre, although there are few recorded measurements to establish a baseline figure for winter water use.

The process of incorporating rice straw into the soil and applying winter water for rice straw decomposition is a very new practice.  Many different techniques of winter water irrigation are currently being tested and used in the estimated 500,000 acres of rice planted each year in California’s Central Valley, and each individual grower has unique water requirements to complete the rice straw decomposition process.

## Estimated Water Use for Rice Straw Decomposition

For the purpose of developing water requirements for CALSIM an estimate of water diversion for winter rice flooding is 1.5 AF/acre and 0.5 AF/acre for non-flooded fields.  These numbers represent the best estimate of water used for rice decomposition after interviewing several rice farmers and water experts in the Sacramento Valley.

The 1.5 AF/ac rate for flooded fields may be on the low side, especially if water is continuously available throughout the season and if the fields are being used for waterfowl/hunting.  Dialogue between environmentalists, waterfowl conservationists, farmers, and researchers have lead to an increased awareness of the potential for coupling waterfowl friendly winter flooding with innovative experimental techniques to manage rice straw.  According to Ducks Unlimited, during the winter of 1999-2000 over 137,000 acres of rice straw was flooded to create wetland habitat for waterfowl.  This represents about 30% of all planted rice acreage in California.  Water that is applied to rice fields in excess of requirements for rice straw decomposition for waterfowl purposes is classified as rice decomposition use.  As of now, it seems that winter water used for rice decomposition and waterfowl habitat are being lumped into one dual-use category.  We have attempted to include additional water use for waterfowl habitat in our estimation of the overall water demand for rice straw decomposition.

The following calculation, Tables, and Chart contain the water use estimate to decompose rice straw.

Sample calculation for 90% flood and 10% non-flood

Annual water requirement 	= (Acreage * 75% (25% is burned) * 90% *1.5 feet )

+ (Acreage * 75% (25% is burned) * 10% *0.5 feet )

Water use estimate for each DSA

Effects of Precipitation on Rice Decomposition Water Demand

The effect of winter precipitation on the amount of water used during field flooding in late October and early November is minimal.   Because it is crucial to add moisture to the straw incorporated soil as soon after harvest as possible to take advantage of warmer temperatures, the majority of water deliveries in early stages of decomposition are unaffected.

However, the considerable precipitation falling in December and January do have an effect on system maintenance demands, and can supplement water deliveries by up to 20% of total water applied in heavy rainfall years.  Scott Tucker, manager of Pelger Mutual Water Company in Sutter County estimates that precipitation contributes 10% to the amount of water applied for rice decomposition.

Drainage of Rice Decomposition Water

Water applied to fields for the purpose of rice decomposition is subject to a variety of losses, including evaporation, transpiration, deep percolation, and runoff.  The factors are not consistent throughout the Sacramento Valley.  As rice fields are drained in February to prepare for tillage.  In some areas of the Sacramento Valley approximately four inches of water (.33 AC-FT/acre) is returned to the system from fields that have used the winter flood incorporation system and some areas report very little drainage.

Estimates of return flow from February drainage are included in the following Tables:

February Drainage Estimates

References

- Bird JA, Eagle AJ, Hair MW, Zilbert E, van Kessle C.  2002.  Long Term Studies Find Benefits, Challenges in Alternative Straw Management, California Agriculture March-April 2002

- Brandon DM, Brouder S, Chaney D, Jill JE, Scardaci SC, Williams, JF.  1995.  Rice Straw Incorporation.  Agronomy Fact Sheet Series 1995-1, Department of Agronomy and Range Science, University of California, Davis

- Brandon DM, Brouder S, Chaney D, Hill JE, Scardaci SC, Williams JF.  1998.  Rice Production in California – Rice Straw Management.  Department of Agronomy and Range Science, University of California, Davis

- Horwath, William R.  2001.  Impact fo Rice Straw Incorporation on Yield Potential-2001.  Department of Land, Air, and Water Resources.  University of California, Davis.

5.  Studer HE, Jenkins BM, Upadhyaya S.  1992.  Methods of Straw

Incorporation.  Department of Biological and Agricultural Engineering,.

University of California, Davis

- J & D Outdoor Communications.  2000.  Rice and Waterfowl.  Ducks Unlimited, Inc; Valley – Bay CARE

- Hill J.  1999.  Integrating Rice Cultural Practices and Waterfowl Habitat.  Department of Agronomy and Range Science, University of California

- California Air Resources Board.  2001.  2001 Report to the Legislature – Progress Report on the Phase-Down and the 1998-2000 Pause in the Phase-Down of Rice Straw Burning in the Sacramento Valley Air Basin.  California Air Resources Board, California Department of Food & Agriculture.

- Schrukraft D, 2002.  Sacramento Valley Fall Burn Report – 2001.  Weathernews Inc., Chico CA.  www.syix.com/rrb/01rpt/FallBurn.htm

- Jack Williams.  Interviewed on April 22, 2003.  UC Extension Service – Sutter County Office, Yuba City, CA

- Scott Tucker.  Interviewed on April 21 and 23, 2003.  Pelger Mutual Water Company, Robbins, CA

- Ben Pennock. Interviewed on April 25, 2003.  Glenn-Colusa Irrigation District

18) 	Describe recent genetic discrimination work conducted by DWR on spring-run Chinook salmon taken at the Skinner Fish Facility and compare the results to the current length size criteria.

DWR has a contract with Oregon State University to research new genetic markers to try to more accurately identify individual spring run in mixed populations.  OSU is also trying to find genetic mechanisms for spring run life history strategy.  At this time DWR is not able to identify individual spring run at the Delta Export Facilities, and not able to make comparisons to length criteria, but expects to be able to by 10/2004.

19)	Describe the individual and cumulative effects of anticipated CVP and SWP water transfers (i.e. EWA, Metropolitan Water District,  and DWR’s Dry Year Program, etc), during the duration of the long term OCAP, on Delta outflow, in Delta circulation patterns, changes in project reservoir storage, changes in the timing of releases, and changes in temperature control operations below project dams. Also, describe how these transfers will be integrated increased releases for the Freeport Project in dry or critical years. What is the effect of all anticipated transfers combined?

In the current CALSIM II EWA 500 cfs of capacity at banks is reserved for EWA transfers from July through September each year.  The source of the water is from Yuba River the effect of the transfers of the will be in the wintertime when the flows from Yuba are reduced Jan – Mar to reflect lower flows due to the late summer transfers.

OCAP is analyzing potential available pumping capacity during the July-Sep period of each year.  Pumping capacities are displayed below at the 6680 cfs and no intertie CALSIM II simulations that were used in the Draft OCAP BA for the today case.  The figures show the capacity available for the range of water years as sorted by the 40-30-30 index going from dry to wet years for total available pumping capacity and then for EI restricted capacities.

Figure X. Tracy total and EI restricted pumping capacity sorted by 40-30-30 Index, post-processed from Draft OCAP Today run

Figure X. Banks total and EI restricted pumping capacity sorted by 40-30-30 Index, post-processed from Draft OCAP Today run

Releases to support the available capacity would have to occur in the July-Sep period.  Since the future amount of transferred water is unknown at this time the above graphs give a maximum pumping amount that could occur within a particular 40-30-30 water year type.  Impacts on temperature and delta requirements would have to be determined for each transfer.

Note that the data shown in the above graphs comes from a preliminary OCAP with out EWA and will be updated with the final results from OCAP.

20)	Since construction of the proposed Rock Slough Intake Fish Screen has been delayed, provide a schedule for completing the design and construction phase.  Include a detailed description of the proposed fish monitoring plan that will meet the requirements of previous biological opinions (NOAA Fisheries: 1993 Winter- run; 1993 Los Vaqueros; 2000 CVPIA opinion; and Fish and Wildlife Service opinions) until this screen is built.

The diversion is presently unscreened and construction of a fish screen is directed under CVPIA and included in the District’s biological opinion for the Los Vaqueros project.  The USBR in collaboration with CCWD is responsible for constructing the fish screen.  Reclamation has requested an extension to the December 2003 deadline to complete the Rock Slough fish screen.  Reclamation is asking for an extension until December 2008 to allow completion of current CALFED project studies that might affect frequency of usage of the Rock Slough intake and therefore the screen design.

# Footnotes

Richardson, T. H., and P. Harrison.  1990.  Fish and Wildlife Impacts of Shasta Dam Water Temperature Control Alternatives.  Prepared for the U.S. Bureau of Reclamation, Sacramento, California.  U.S. FWS--Fish and Wildlife Enhancement, Sacramento, California.