| JOB HAZARD ANALYSIS (INSTRUCTION ON REVERSE SIDE) | JOB TITLE (and number if applicable): BARBED WIRE INSTALLATION | PAGE 1 OF 1 JHA NO. | DATE: 6/21/2000 | NEW REVISED |
| --- | --- | --- | --- | --- |
| COMPANY/ORGANIZATION: USBR - MPCO | PLANT/LOCATION: MP Construction Office - Willows | DEPARTMENT: |
| TITLE OF PERSON WHO DOES JOB: A Penna | SUPERVISOR: R. Welsh | REQUIRED AND/OR RECOMMENDED PERSONAL PROTECTIVE EQUIPMENT: Gloves, Safety Glasses. Other equipment: Ladder, GFCI, extension cord, drill, & wire cutters. |
| ANALYSIS BY: A. Penna | REVIEWED BY: R. Donahue | APPROVED BY: S. Marquez |
| GENERAL INSTRUCTIONS: Add sections of barbed wire from existing fence to building - Security Enhancement |
| OPERATION SEQUENCE: | EQUIPMENT, TOOLS, AND ALL FACILITIES INVOLVED: | POTENTIAL HAZARDS: | RECOMMENDED ACTION OR PROCEDURE: | REFERENCES: |
| Transport Barbed Wire | None | Cuts from wire, wire uncoiling. Insect/Snake bites Over-exertion | Wear leather gloves and eye protection. Control wire to prevent a backlash. Check for insect/snakes as wire has been stored outside. Use buddy system for lifting | RSHS 8.3, 8.6, 7.14.9 |
| Drill Holes for Eye Bolts | Drill, extension cord, step ladder | Electrical shock and falls | Check cord and drill for defects. Use GFCI. Ensure ladder is in good condition, stable, and do not over- reach | RSHS 12.2.6, 12.4, 13.14.8, 16.1, |
| String Barbed Wire | Ladder, wire cutters | Cuts from wire, wire uncoiling, falls. | Wear leather gloves and eye protection. Ensure ladder is in good condition, stable, and do not over-reach | RSHS 8.3, 8.6, 13.14.8 |