Reclamation Sustainable Design Requirements Flowchart 
for Buildings (New Construction & Major Renovations)

# Text boxes

Must meet sustainable purchasing requirements 1a, 1b

Note:  For any project using appropriated funds

04/04/2013

(Go Both Directions)

- Meter is required for each type of energy use (electric, gas, steam) where cost effective 2

- Meter is encouraged for indoor water use 2

- Meter is encouraged for significant outdoor water use 2

Will Reclamation own the building?

Note:  “Transferred Works” projects are still owned by Reclamation.

No

No sustainable design requirements unless required by the owner

Yes

Will the building be a “Reclamation EISA Covered Facility”?

Note:  Must pay for utilities (energy and/or water)

Yes

Must meet Reclamation determined energy & water use requirements to meet EO 13514 greenhouse gas emissions and EISA requirements for Reclamation as a whole if being included in those calculations 5, 6

No

Implement applicable “Guiding Principles” where cost effective 3, 4

No

Will the building be greater than 5,000 ft2?

Yes

No

Is the project a Major Renovation?

Is this a New Construction project?

No

Yes

Yes

No

Is the major renovation for a purpose other than restoring a historic building or correcting existing health, sanitary or safety code violations?

(Go Both Directions)

Must meet EISA 2007 fossil fuel reduction requirements 7b

Will the building cost more than $2,500,000? 7a

No

Will the disturbed ground area be 5,000 ft2 or more?

Note:  Disturbed ground area includes building footprint and all surrounding disturbed areas.

No

Yes

Yes

Must meet “Guiding Principles” and “Reclamation Specific (RS) Focus Areas and Initiatives”  3, 4

Yes

References

1a - Sustainable purchasing:  Procurement ET

(see Procurement ET Attachment)

1b - Sustainable purchasing:  Sustainable Facilities Tool

2 - Meters:  EPAct 2005, Section 103

3 - Reclamation SBIP:  Reclamation Sustainable Buildings Website

4 - Guiding Principles Checklists:  Reclamation Sustainable Buildings Website

5 - EISA Agency Energy Reduction:  EISA 2007 Section 431

6 - Greenhouse Gas Emissions:  EO 13514 Section 2

7a - Fossil Fuels:  EISA 2007 Section 433(a)(D)(i)

7b - Fossil Fuels:  EISA 2007 Section 433(a)(D)(i)(I)

8 - Site Hydrology:  EISA 2007 Section 438

This document:  USBR Sustainable Buildings External Website

Must meet EISA 2007 site hydrology requirements 8

Definitions:

Transferred Works:  Buildings and structures owned by Reclamation, but operated by a non-Federal party under contract.

Reserved Works:  Buildings and structures owned, occupied, and operated by Reclamation.  While Reclamation is only currently include “Reserved Works” buildings in its energy reduction calculations for existing buildings, exempting transferred works does not apply to new construction.

EISA:  Energy Independence and Security Act of 2007

Major Renovation:  A major renovation project is one with a “Field Cost” of 50% or more of the building’s Current Replacement Value (CRV).